## Slide 1: Sistemas de protección contra caídas II
Prevención de caídas en la construcción
Criterios y prácticas

## Slide 2: Objetivos de aprendizaje 1
Comprensión de las prácticas recomendadas básicas asociadas con los sistemas de protección contra caídas siguientes:
    Dispositivos de posicionamiento
    Retención de caídas
    Líneas de advertencia
    Zonas de acceso controlado
Sistemas de protección contra caídas II

## Slide 3: Objetivos de aprendizaje 2
Comprensión de las prácticas recomendadas básicas asociadas con los sistemas de protección contra caídas siguientes:
    Sistemas de control de seguridad
    Cubiertas
    Protección contra caída de objetos
    Plan de protección contra caídas
    Requisitos de capacitación de protección contra caídas
Sistemas de protección contra caídas II

## Slide 4: Preguntas básicas 1
¿A cuántos pies desde un borde sin protección se considera protección contra caídas?
    Es decir, ¿qué distancia de un riesgo de caída es suficiente para no necesitar un sistema de protección?
Sistemas de protección contra caídas II

## Slide 5: Preguntas básicas 2
No hay una distancia segura con respecto a ningún borde sin protección.
¿A cuántos pies desde un borde sin protección se considera protección contra caídas?
    Es decir, ¿qué distancia de un riesgo de caída es suficiente para no necesitar un sistema de protección?
Sistemas de protección contra caídas II

## Slide 6: Sistemas de dispositivos de posicionamiento
La OSHA define un sistema de dispositivos de posicionamiento como un sistema de arnés corporal o cinturón de seguridad instalado para permitir que un trabajador se apoye en una superficie vertical elevada, como una pared, con ambas manos libres mientras se inclina.
Los sistemas de arnés corporal o cinturón de seguridad deben colocarse de manera que un trabajador pueda caer libremente no más de 2 pies.
    ¡LA PRÁCTICA RECOMENDADA ES DEJAR DE UTILIZAR CINTURONES DE SEGURIDAD!
Los arneses corporales o cinturones de seguridad deben fijarse a un anclaje capaz de soportar al menos el doble de la carga de impacto potencial de la caída de un trabajador o 3,000 libras, lo que sea mayor.
Sistemas de protección contra caídas II
Notes: 1926.502(e)(2)Positioning devices shall be secured to an anchorage capable of supporting at least twice the potential impact load of an employee's fall or 3,000 pounds (13.3 kN), whichever is greater.

## Slide 7: Sistemas de retención de caídas 1
Aunque los sistemas de retención de caídas no se mencionan en la Subparte M, la OSHA reconoce un sistema de retención de caídas como medio de prevención. El sistema, si se utiliza correctamente, ata a un trabajador de manera que no permita una caída de ninguna distancia.
    Este sistema se compone de un cinturón de seguridad o arnés corporal, un anclaje, conectores y otros equipos necesarios. Otros componentes suelen ser una cuerda de seguridad, una cuerda salvavidas y otros dispositivos.
    Para que un sistema de retención funcione, el anclaje debe ser lo suficientemente fuerte como para impedir que el trabajador se desplace más allá del punto en el que el sistema está totalmente extendido, incluido un factor de seguridad adecuado.
Sistemas de protección contra caídas II
Notes: 1926.502(d)"Personal fall arrest systems." Personal fall arrest systems and their use shall comply with the provisions set forth below. Effective January 1, 1998, body belts are not acceptable as part of a personal fall arrest system. Note: The use of a body belt in a positioning device system is acceptable and is regulated under paragraph (e) of this section.

## Slide 8: Sistemas de retención de caídas 2
La retención de caídas presupone que el trabajador no puede alcanzar el borde.
Básicamente, está atado con una correa corta.
Si el empleado pudiera alcanzar el borde y caer por encima de él, debe considerarse en detención de caídas.
Requisitos de seguridad 1910.140(b) y ANSI/ASSP Z359.15-2014 para cuerdas salvavidas de anclaje único y anticaídas para sistemas personales de detención de caídas.
Sistemas de protección contra caídas II

## Slide 9: Sistemas de líneas de advertencia 1
La OSHA define un sistema de líneas de advertencia como una barrera instalada en un techo para advertir a los trabajadores que se están acercando a un lado o borde del techo sin protección, y para designar una zona en la que se pueden realizar trabajos de techado sin utilizar barandas, arneses corporales o sistemas de redes de seguridad para proteger a los trabajadores en la zona.
    Los sistemas de líneas de advertencia consisten en sogas, cables o cadenas, además de montantes de soporte.
Sistemas de protección contra caídas II
Notes: 1926.502(f)"Warning line systems." Warning line systems [See 1926.501(b)(10)] and their use shall comply with the following provisions:
1926.502(f)(1)The warning line shall be erected around all sides of the roof work area.
1926.502(f)(1)(i)When mechanical equipment is not being used, the warning line shall be erected not less than 6 feet (1.8 m) from the roof edge.
1926.502(f)(1)(ii)When mechanical equipment is being used, the warning line shall be erected not less than 6 feet (1.8 m) from the roof edge which is parallel to the direction of mechanical equipment operation, and not less than 10 feet (3.1 m) from the roof edge which is perpendicular to the direction of mechanical equipment operation.
1926.502(f)(1)(iii)Points of access, materials handling areas, storage areas, and hoisting areas shall be connected to the work area by an access path formed by two warning lines.
1926.502(f)(1)(iv)When the path to a point of access is not in use, a rope, wire, chain, or other barricade, equivalent in strength and height to the warning line, shall be placed across the path at the point where the path intersects the warning line erected around the work area, or the path shall be offset such that a person cannot walk directly into the work area.
1926.502(f)(2)Warning lines shall consist of ropes, wires, or chains, and supporting stanchions erected as follows:
1926.502(f)(2)(i)The rope, wire, or chain shall be flagged at not more than 6-foot (1.8 m) intervals with high-visibility material;
1926.502(f)(2)(ii)The rope, wire, or chain shall be rigged and supported in such a way that its lowest point (including sag) is no less than 34 inches (.9 m) from the walking/working surface and its highest point is no more than 39 inches (1.0 m) from the walking/working surface;
1926.502(f)(2)(iii)After being erected, with the rope, wire, or chain attached, stanchions shall be capable of resisting, without tipping over, a force of at least 16 pounds (71 N) applied horizontally against the stanchion, 30 inches (.8 m) above the walking/working surface, perpendicular to the warning line, and in the direction of the floor, roof, or platform edge;
1926.502(f)(2)(iv)The rope, wire, or chain shall have a minimum tensile strength of 500 pounds (2.22 kN), and after being attached to the stanchions, shall be capable of supporting, without breaking, the loads applied to the stanchions as prescribed in paragraph (f)(2)(iii) of this section; and
1926.502(f)(2)(v)The line shall be attached at each stanchion in such a way that pulling on one section of the line between stanchions will not result in slack being taken up in adjacent sections before the stanchion tips over.

## Slide 10: Sistemas de líneas de advertencia 2
Las líneas de advertencia se deben colocar alrededor de todos los costados de las áreas de trabajo en el techo.
Cuando no se utilicen equipos mecánicos, la línea de advertencia debe estar instalada al menos a 6 pies desde el borde del techo.
Cuando se utilicen equipos mecánicos, deberá colocarse la línea de advertencia:
    A una distancia mínima de 6 pies desde el borde del techo paralela a la dirección de funcionamiento del equipo mecánico.
    A una distancia mínima de 10 pies desde el borde del techo perpendicular a la dirección de funcionamiento del equipo mecánico.
Sistemas de protección contra caídas II
Notes: 1926.502(f)"Warning line systems." Warning line systems [See 1926.501(b)(10)] and their use shall comply with the following provisions:
1926.502(f)(1)The warning line shall be erected around all sides of the roof work area.
1926.502(f)(1)(i)When mechanical equipment is not being used, the warning line shall be erected not less than 6 feet (1.8 m) from the roof edge.
1926.502(f)(1)(ii)When mechanical equipment is being used, the warning line shall be erected not less than 6 feet (1.8 m) from the roof edge which is parallel to the direction of mechanical equipment operation, and not less than 10 feet (3.1 m) from the roof edge which is perpendicular to the direction of mechanical equipment operation.
1926.502(f)(1)(iii)Points of access, materials handling areas, storage areas, and hoisting areas shall be connected to the work area by an access path formed by two warning lines.
1926.502(f)(1)(iv)When the path to a point of access is not in use, a rope, wire, chain, or other barricade, equivalent in strength and height to the warning line, shall be placed across the path at the point where the path intersects the warning line erected around the work area, or the path shall be offset such that a person cannot walk directly into the work area.
1926.502(f)(2)Warning lines shall consist of ropes, wires, or chains, and supporting stanchions erected as follows:
1926.502(f)(2)(i)The rope, wire, or chain shall be flagged at not more than 6-foot (1.8 m) intervals with high-visibility material;
1926.502(f)(2)(ii)The rope, wire, or chain shall be rigged and supported in such a way that its lowest point (including sag) is no less than 34 inches (.9 m) from the walking/working surface and its highest point is no more than 39 inches (1.0 m) from the walking/working surface;
1926.502(f)(2)(iii)After being erected, with the rope, wire, or chain attached, stanchions shall be capable of resisting, without tipping over, a force of at least 16 pounds (71 N) applied horizontally against the stanchion, 30 inches (.8 m) above the walking/working surface, perpendicular to the warning line, and in the direction of the floor, roof, or platform edge;
1926.502(f)(2)(iv)The rope, wire, or chain shall have a minimum tensile strength of 500 pounds (2.22 kN), and after being attached to the stanchions, shall be capable of supporting, without breaking, the loads applied to the stanchions as prescribed in paragraph (f)(2)(iii) of this section; and
1926.502(f)(2)(v)The line shall be attached at each stanchion in such a way that pulling on one section of the line between stanchions will not result in slack being taken up in adjacent sections before the stanchion tips over.

## Slide 11: Sistemas de líneas de advertencia 3
Las líneas de advertencia deben colocarse antes de comenzar el trabajo.
Todos los trabajadores deben recibir capacitación. 1926.503(a)(2)
No se debe trabajar fuera de las líneas de advertencia sin protección contra caídas. 1926.502(f)(3)
Pueden utilizarse en techos planos y con poca pendiente. 1926.501(b)(10)
El control de seguridad debe utilizarse con moderación.
Los empleados deben cumplir con las advertencias e instrucciones de inmediato. 1926.502(h)(4)
Sistemas de protección contra caídas II
Notes: 1926.502(f)"Warning line systems." Warning line systems [See 1926.501(b)(10)] and their use shall comply with the following provisions:
1926.502(f)(1)The warning line shall be erected around all sides of the roof work area.
1926.502(f)(1)(i)When mechanical equipment is not being used, the warning line shall be erected not less than 6 feet (1.8 m) from the roof edge.
1926.502(f)(1)(ii)When mechanical equipment is being used, the warning line shall be erected not less than 6 feet (1.8 m) from the roof edge which is parallel to the direction of mechanical equipment operation, and not less than 10 feet (3.1 m) from the roof edge which is perpendicular to the direction of mechanical equipment operation.
1926.502(f)(1)(iii)Points of access, materials handling areas, storage areas, and hoisting areas shall be connected to the work area by an access path formed by two warning lines.
1926.502(f)(1)(iv)When the path to a point of access is not in use, a rope, wire, chain, or other barricade, equivalent in strength and height to the warning line, shall be placed across the path at the point where the path intersects the warning line erected around the work area, or the path shall be offset such that a person cannot walk directly into the work area.
1926.502(f)(2)Warning lines shall consist of ropes, wires, or chains, and supporting stanchions erected as follows:
1926.502(f)(2)(i)The rope, wire, or chain shall be flagged at not more than 6-foot (1.8 m) intervals with high-visibility material;
1926.502(f)(2)(ii)The rope, wire, or chain shall be rigged and supported in such a way that its lowest point (including sag) is no less than 34 inches (.9 m) from the walking/working surface and its highest point is no more than 39 inches (1.0 m) from the walking/working surface;
1926.502(f)(2)(iii)After being erected, with the rope, wire, or chain attached, stanchions shall be capable of resisting, without tipping over, a force of at least 16 pounds (71 N) applied horizontally against the stanchion, 30 inches (.8 m) above the walking/working surface, perpendicular to the warning line, and in the direction of the floor, roof, or platform edge;
1926.502(f)(2)(iv)The rope, wire, or chain shall have a minimum tensile strength of 500 pounds (2.22 kN), and after being attached to the stanchions, shall be capable of supporting, without breaking, the loads applied to the stanchions as prescribed in paragraph (f)(2)(iii) of this section; and
1926.502(f)(2)(v)The line shall be attached at each stanchion in such a way that pulling on one section of the line between stanchions will not result in slack being taken up in adjacent sections before the stanchion tips over.

## Slide 12: Sistemas de líneas de advertencia 4
La cuerda, el cable o la cadena deben estar señalizados a intervalos de no más de 6 pies con material de alta visibilidad y tener una resistencia mínima de 500 libras.
La cuerda, el cable o la cadena deben estar montados y soportados de manera que:
    El punto más bajo (incluida la inclinación) esté al menos a 34 pulgadas desde la superficie de trabajo o de paso.
    Su punto más alto no esté a más de 39 pulgadas desde la superficie de trabajo o de paso.
    Si se tira de una sección de la línea entre las barras, la cuerda no se tensará en la sección adyacente antes de que vuelquen las barras.
Las barras, después de haber sido equipadas con líneas de advertencia, deben poder resistir, sin volcarse, una fuerza de al menos 16 libras aplicada horizontalmente contra la barra, 30 pulgadas por encima de la superficie de trabajo o de paso, perpendicular a la línea de advertencia y en dirección al suelo, techo o borde de la plataforma.
1926.502(f)(2)
Sistemas de protección contra caídas II
Notes: 1926.502(f)"Warning line systems." Warning line systems [See 1926.501(b)(10)] and their use shall comply with the following provisions:
1926.502(f)(1)The warning line shall be erected around all sides of the roof work area.
1926.502(f)(1)(i)When mechanical equipment is not being used, the warning line shall be erected not less than 6 feet (1.8 m) from the roof edge.
1926.502(f)(1)(ii)When mechanical equipment is being used, the warning line shall be erected not less than 6 feet (1.8 m) from the roof edge which is parallel to the direction of mechanical equipment operation, and not less than 10 feet (3.1 m) from the roof edge which is perpendicular to the direction of mechanical equipment operation.
1926.502(f)(1)(iii)Points of access, materials handling areas, storage areas, and hoisting areas shall be connected to the work area by an access path formed by two warning lines.
1926.502(f)(1)(iv)When the path to a point of access is not in use, a rope, wire, chain, or other barricade, equivalent in strength and height to the warning line, shall be placed across the path at the point where the path intersects the warning line erected around the work area, or the path shall be offset such that a person cannot walk directly into the work area.
1926.502(f)(2)Warning lines shall consist of ropes, wires, or chains, and supporting stanchions erected as follows:
1926.502(f)(2)(i)The rope, wire, or chain shall be flagged at not more than 6-foot (1.8 m) intervals with high-visibility material;
1926.502(f)(2)(ii)The rope, wire, or chain shall be rigged and supported in such a way that its lowest point (including sag) is no less than 34 inches (.9 m) from the walking/working surface and its highest point is no more than 39 inches (1.0 m) from the walking/working surface;
1926.502(f)(2)(iii)After being erected, with the rope, wire, or chain attached, stanchions shall be capable of resisting, without tipping over, a force of at least 16 pounds (71 N) applied horizontally against the stanchion, 30 inches (.8 m) above the walking/working surface, perpendicular to the warning line, and in the direction of the floor, roof, or platform edge;
1926.502(f)(2)(iv)The rope, wire, or chain shall have a minimum tensile strength of 500 pounds (2.22 kN), and after being attached to the stanchions, shall be capable of supporting, without breaking, the loads applied to the stanchions as prescribed in paragraph (f)(2)(iii) of this section; and
1926.502(f)(2)(v)The line shall be attached at each stanchion in such a way that pulling on one section of the line between stanchions will not result in slack being taken up in adjacent sections before the stanchion tips over.

## Slide 13: Zonas de acceso controlado 1
Una zona de acceso controlado es un área de trabajo en la que pueden realizarse determinados tipos de trabajos sin utilizar sistemas convencionales de protección contra caídas. 1926.502(g)
    albañilería en alto y trabajos relacionados;
    trabajo en bordes salientes;
    construcción residencial, y
    montaje de prefabricados de hormigón.
El acceso de los trabajadores a estas zonas debe controlarse cuidadosamente.
    Por ejemplo, se designaría una zona de acceso controlado donde se estuvieran realizando trabajos de albañilería en alto sin la protección de barandas. En este ejemplo, solo los albañiles y otros trabajadores que realmente se dedican a la albañilería tendrían permiso para ingresar a la zona de acceso controlado.
    Cuando se utilicen para controlar el acceso a zonas en las que se estén realizando trabajos en bordes salientes y de otro tipo, las zonas de acceso controlado deben definirse mediante una línea de control o cualquier otro medio que restrinja el acceso.
Sistemas de protección contra caídas II

## Slide 14: Zonas de acceso controlado 2
Cuando se utilicen líneas de control para delimitar una zona de acceso controlado, deberán instalarse a una distancia mínima de 6 pies y máxima de 25 pies del borde sin protección o saliente, excepto cuando se presenten las siguientes situaciones:
    Cuando se estén instalando elementos prefabricados de hormigón, la línea de control se instalará a una distancia mínima de 6 pies y máxima de 60 pies o la mitad de la longitud del elemento que se esté instalando, la que sea menor, desde el borde saliente.
La línea de control debe extenderse a lo largo de toda la longitud, ser aproximadamente paralela al lado sin protección o el borde saliente y estar conectada a cada uno con un sistema de barandas o pared.
1926.502(g)(1)
Sistemas de protección contra caídas II

## Slide 15: Zonas de acceso controlado 3
Cuando se utilicen zonas de acceso controlado para limitar el ingreso a zonas en las que se realicen trabajos de albañilería en alto y trabajos relacionados:
    Se debe instalar una línea de control para definir la zona de trabajo y se debe instalar a una distancia mínima de 10 pies y máxima de 15 pies del borde de trabajo.
    Las líneas de control deben instalarse aproximadamente paralelas al borde del trabajo y deben extenderse a una distancia suficiente para rodear a todos los trabajadores que realicen trabajos de albañilería en alto y trabajos relacionados en el borde de trabajo.
    Deberán instalarse líneas de control adicionales en cada extremo de la zonas de acceso controlado para delimitar el área de trabajo.
    En la zona de acceso controlado, solo se permite la presencia de trabajadores que realicen trabajos de albañilería en alto o trabajos relacionados.
    1926.502(g)(2)
Sistemas de protección contra caídas II

## Slide 16: Zonas de acceso controlado 4
Las líneas de control deben consistir en cuerdas, cables, cintas o materiales equivalentes, y barras de soporte. Cuando se utilice, cada línea de control deberá:
    Estar señalizada o marcada claramente de otro modo a intervalos de no más de 6 pies con material de alta visibilidad.
    Estar montada y apoyada de tal manera que el punto más bajo (incluida la inclinación) no esté a menos de 39 pulgadas de la superficie de trabajo o de paso, y el punto más alto no esté a más de 45 pulgadas, o a más de 50 pulgadas, cuando se realicen operaciones de albañilería en alto, desde la superficie de trabajo o de paso.
    Tener una resistencia a la rotura de al menos 200 libras.
Sistemas de protección contra caídas II

## Slide 17: Sistemas de control de seguridad 1
Un sistema de control de seguridad utiliza a una persona competente como control de seguridad que puede reconocer y advertir a los trabajadores de los riesgos de caídas.
Los sistemas de control de seguridad suelen utilizarse como parte de los planes de protección contra caídas durante los trabajos de montaje de prefabricados de hormigón, los trabajos en bordes salientes y los trabajos de construcción residencial cuando la protección convencional contra caídas sea inviable o creara un peligro mayor y no se utilizan medidas alternativas (como andamios, escaleras móviles o plataformas de trabajo montadas en vehículos).
Sistemas de protección contra caídas II

## Slide 18: Sistemas de control de seguridad 2
Cuando se realicen trabajos de techado en un techo plano o con poca pendiente que tenga un ancho de 50 pies o menos, se puede utilizar un sistema de control de seguridad como técnica independiente de protección contra caídas.
Solo se permite la presencia de trabajadores que realicen trabajos de techado de pendiente baja y trabajadores que realicen las tarea específicas del trabajo cubiertas por un plan de protección contra caídas en una zona en la que los trabajadores estén siendo protegidos por un sistema de control de seguridad.
El encargado del control de seguridad no puede estar realizando otras tareas mientras sea quien controle la seguridad.
Sistemas de protección contra caídas II
Notes: 1926.502(h)(1)The employer shall designate a competent person to monitor the safety of other employees and the employer shall ensure that the safety monitor complies with the following requirements:
1926.502(h)(1)(i)The safety monitor shall be competent to recognize fall hazards;
1926.502(h)(1)(ii)The safety monitor shall warn the employee when it appears that the employee is unaware of a fall hazard or is acting in an unsafe manner;
1926.502(h)(1)(iii)The safety monitor shall be on the same walking/working surface and within visual sighting distance of the employee being monitored;
1926.502(h)(1)(iv)The safety monitor shall be close enough to communicate orally with the employee; and
1926.502(h)(1)(v)The safety monitor shall not have other responsibilities which could take the monitor's attention from the monitoring function.
1926.502(h)(2)Mechanical equipment shall not be used or stored in areas where safety monitoring systems are being used to monitor employees engaged in roofing operations on low-slope roofs.
1926.502(h)(3)No employee, other than an employee engaged in roofing work [on low-sloped roofs] or an employee covered by a fall protection plan, shall be allowed in an area where an employee is being protected by a safety monitoring system.
1926.502(h)(4)Each employee working in a controlled access zone shall be directed to comply promptly with fall hazard warnings from safety monitors.

## Slide 19: Sistemas de control de seguridad 3
El trabajador designado como encargado del control de seguridad:
    No podrá realizar otras tareas laborales que puedan desviar su atención de la función de control.
    Debe estar en la misma superficie y a la vista de los empleados.
    Debe estar lo suficientemente cerca como para comunicarse oralmente con los empleados.
El encargado del control de seguridad no puede estar realizando otras tareas mientras sea quien controle la seguridad.
Sistemas de protección contra caídas II
Notes: 1926.502(h)(1)The employer shall designate a competent person to monitor the safety of other employees and the employer shall ensure that the safety monitor complies with the following requirements:
1926.502(h)(1)(i)The safety monitor shall be competent to recognize fall hazards;
1926.502(h)(1)(ii)The safety monitor shall warn the employee when it appears that the employee is unaware of a fall hazard or is acting in an unsafe manner;
1926.502(h)(1)(iii)The safety monitor shall be on the same walking/working surface and within visual sighting distance of the employee being monitored;
1926.502(h)(1)(iv)The safety monitor shall be close enough to communicate orally with the employee; and
1926.502(h)(1)(v)The safety monitor shall not have other responsibilities which could take the monitor's attention from the monitoring function.
1926.502(h)(2)Mechanical equipment shall not be used or stored in areas where safety monitoring systems are being used to monitor employees engaged in roofing operations on low-slope roofs.
1926.502(h)(3)No employee, other than an employee engaged in roofing work [on low-sloped roofs] or an employee covered by a fall protection plan, shall be allowed in an area where an employee is being protected by a safety monitoring system.
1926.502(h)(4)Each employee working in a controlled access zone shall be directed to comply promptly with fall hazard warnings from safety monitors.

## Slide 20: Sistemas de control de seguridad 4
Pueden utilizarse en techos planos y con poca pendiente.
El control de seguridad debe utilizarse con moderación.
Los empleados deben cumplir con las advertencias e instrucciones de inmediato.
Las secciones del techo que se designen para su protección bajo control de seguridad deben tener un ancho inferior a 50 pies.
Los techos más grandes pueden dividirse en secciones.
Sistemas de protección contra caídas II
Notes: 1926.502(h)(1)The employer shall designate a competent person to monitor the safety of other employees and the employer shall ensure that the safety monitor complies with the following requirements:
1926.502(h)(1)(i)The safety monitor shall be competent to recognize fall hazards;
1926.502(h)(1)(ii)The safety monitor shall warn the employee when it appears that the employee is unaware of a fall hazard or is acting in an unsafe manner;
1926.502(h)(1)(iii)The safety monitor shall be on the same walking/working surface and within visual sighting distance of the employee being monitored;
1926.502(h)(1)(iv)The safety monitor shall be close enough to communicate orally with the employee; and
1926.502(h)(1)(v)The safety monitor shall not have other responsibilities which could take the monitor's attention from the monitoring function.
1926.502(h)(2)Mechanical equipment shall not be used or stored in areas where safety monitoring systems are being used to monitor employees engaged in roofing operations on low-slope roofs.
1926.502(h)(3)No employee, other than an employee engaged in roofing work [on low-sloped roofs] or an employee covered by a fall protection plan, shall be allowed in an area where an employee is being protected by a safety monitoring system.
1926.502(h)(4)Each employee working in a controlled access zone shall be directed to comply promptly with fall hazard warnings from safety monitors.

## Slide 21: Cubiertas 1
Un hueco es un agujero o vacío de 2 pulgadas o más en su dimensión mínima en un suelo, techo, cobertizo u otra superficie de trabajo o de paso que es peligroso porque:
    Los trabajadores pueden caerse por el hueco.
    El diseño del hueco puede crear peligro de tropiezo.
    Pueden caer objetos por el hueco y lesionar a los trabajadores que están debajo.
Los trabajadores están protegidos de los peligros asociados con huecos mediante el uso de cubiertas, sistemas personales de protección contra caídas o de barandas.
Sistemas de protección contra caídas II
Notes: 1926.502(i)"Covers." Covers for holes in floors, roofs, and other walking/working surfaces shall meet the following requirements:
1926.502(i)(1)Covers located in roadways and vehicular aisles shall be capable of supporting, without failure, at least twice the maximum axle load of the largest vehicle expected to cross over the cover.
1926.502(i)(2)All other covers shall be capable of supporting, without failure, at least twice the weight of employees, equipment, and materials that may be imposed on the cover at any one time.
1926.502(i)(3)All covers shall be secured when installed so as to prevent accidental displacement by the wind, equipment, or employees.
1926.502(i)(4)All covers shall be color coded or they shall be marked with the word "HOLE" or "COVER" to provide warning of the hazard. Note: This provision does not apply to cast iron manhole covers or steel grates used on streets or roadways.

## Slide 22: Cubiertas 2
Sistemas de protección contra caídas II
Notes: 1926.502(i)"Covers." Covers for holes in floors, roofs, and other walking/working surfaces shall meet the following requirements:
1926.502(i)(1)Covers located in roadways and vehicular aisles shall be capable of supporting, without failure, at least twice the maximum axle load of the largest vehicle expected to cross over the cover.
1926.502(i)(2)All other covers shall be capable of supporting, without failure, at least twice the weight of employees, equipment, and materials that may be imposed on the cover at any one time.
1926.502(i)(3)All covers shall be secured when installed so as to prevent accidental displacement by the wind, equipment, or employees.
1926.502(i)(4)All covers shall be color coded or they shall be marked with the word "HOLE" or "COVER" to provide warning of the hazard. Note: This provision does not apply to cast iron manhole covers or steel grates used on streets or roadways.

## Slide 23: Cubiertas 3
Los siguientes tipos de huecos son habituales en las obras de construcción:
    Huecos cortados (o construidos) en los suelos para recibir equipos o conductos y para futuros puntos de acceso (por ejemplo, aberturas para escaleras que se instalarán más adelante).
    Huecos cortados en techos para preparar la instalación de claraboyas, unidades de ventilación y otros elementos o equipos.
    Excavaciones para fosas, pozos o cigüeñales (por ejemplo, cámaras de aire comprimido).
    Excavaciones o cortes en calzadas.
Sistemas de protección contra caídas II

## Slide 24: Cubiertas 4
Las cubiertas para huecos eficaces son: 1926.502(i)
    Suficientemente grandes como para proporcionar el solapamiento adecuado a fin de evitar que los trabajadores caigan a través de este.
    Suficientemente resistentes como para soportar al menos el doble de peso previsto de la carga más pesada.
    Se dejan sobre el hueco hasta que sea necesario acceder.
    Se inspeccionan con periodicidad para identificar posibles deterioros.
    Aseguradas (lado a lado, y arriba y abajo) y no crean peligro de tropiezo.
    Claramente señalizadas como coberturas de huecos. (Considerar la señalización en otros idiomas)
Sistemas de protección contra caídas II

## Slide 25: Protección contra caída de objetos 1
Las tablas de capellada, cuando se utilicen como protección contra la caída de objetos, se instalarán a lo largo del borde de la superficie de trabajo o de paso para proteger a los empleados que se encuentren debajo.
    Por lo menos 50 libras aplicadas en cualquier dirección hacia abajo o hacia afuera en cualquier punto a lo largo de la tabla de capellada.
    Mínimo de 3 1/2 pulgadas de altura vertical desde su borde superior hasta el nivel de la superficie de trabajo o de paso.
    No deben tener más de 1/4 pulgada de espacio libre por encima de la superficie de trabajo o de paso.
    Deben ser lisas o tener aberturas que no superen 1 pulgada (2.5 cm) en su dimensión mayor.
Sistemas de protección contra caídas II

## Slide 26: Protección contra caída de objetos 2
1926.502(j)(1)
Cuando las herramientas, los equipos o los materiales se apilan a una altura superior a la del borde superior de una tabla de capellada, deben instalarse paneles o pantallas desde la superficie de trabajo o de paso, o la tabla de capellada hasta la parte superior de la baranda superior o larguero intermedio de un sistema de barandas, a una distancia suficiente como para proteger a los empleados que se encuentren debajo.
Sistemas de protección contra caídas II

## Slide 27: Protección contra caída de objetos 3
Los sistemas de barandas, cuando se utilicen como protección contra la caída de objetos, deberán tener todas las aberturas lo suficientemente pequeñas como para impedir el paso de posibles objetos que podrían caer. 1926.502(j)(5)
Durante la realización de trabajos de albañilería en alto y trabajos relacionados:
    No se almacenarán materiales o equipos, excepto mampostería y mortero, a menos de 4 pies (1.2 m) del borde de trabajo.
    El exceso de morteros, las unidades de mampostería rotas o esparcidas y todos los demás materiales y escombros se mantendrán alejados del área de trabajo mediante su retirada a intervalos regulares. 1926.502(j)(6)
Sistemas de protección contra caídas II

## Slide 28: Protección contra caída de objetos 4
Durante la realización de trabajos en techos:
    Los materiales y equipos no se almacenarán a menos de 6 pies (1.8 m) del borde de un techo, a menos que se instalen barandas en el borde.
    Los materiales apilados, agrupados o colocados cerca del borde del techo deben ser estables y mantenerse por sí solos.
Las capotas, cuando se las utiliza como protección contra la caída de objetos, deberán ser lo suficientemente resistentes como para evitar el desplome y la penetración de cualquier objeto que podría caer sobre la capota.
Sistemas de protección contra caídas II

## Slide 29: Plan de protección contra caídas 1
Permitido para:
    trabajos en bordes salientes
    montaje de prefabricados de hormigón
    construcción residencial
Los planes de caída por escrito específicos de la obra se consideran una alternativa para estas actividades.
Sistemas de protección contra caídas II

## Slide 30: Plan de protección contra caídas 2
Si el empleador puede demostrar que los sistemas de protección contra caídas requeridos son inviables o crean un peligro mayor, el empleador debe, en su lugar, desarrollar e implementar un plan de protección contra caídas específico para el lugar de trabajo por escrito de acuerdo con el Título 29 del CFR, parte 1926.502(k).
    La OSHA no considera que la “inviabilidad económica” sea una base para no proporcionar protección convencional contra caídas.
    Nota: existe la presunción de que es factible y no creará un peligro mayor implementar al menos uno de los sistemas de protección contra caídas.
Sistemas de protección contra caídas II

## Slide 31: Plan de protección contra caídas 3
Sistemas de protección contra caídas II

## Slide 32: Plan de protección contra caídas 4
Escrito por una persona calificada.
Debe identificar cada lugar en el que no puedan utilizarse sistemas de protección contra caídas convencionales y los designarán como Zonas de acceso controlado (Controlled Access Zones, CAZ).
Implementará un sistema de control de seguridad donde no se haya implementado ninguna otra medida alternativa.
Identificará a todos los trabajadores designados para trabajar en la CAZ.
Se revisará y actualizará según proceda si se produce una caída o un cuasi accidente.
Sistemas de protección contra caídas II

## Slide 33: Plan de protección contra caídas 5
En el Apéndice E de la Subparte M de la Norma OSHA, se proporcionan ejemplos de los planes contra caídas para lo siguiente:
    construcción residencial, y
    montaje de prefabricados de hormigón.
Sistemas de protección contra caídas II

## Slide 34: Requisitos de capacitación de protección contra caídas 1
El empleador deberá proporcionar un programa de capacitación para cada empleado que podría estar expuesto a riesgos de caídas.
    Capacitar a cada empleado para reconocer los riesgos de caída.
    Utilizar los procedimientos adecuados que deben seguirse para minimizar estos peligros.
Sistemas de protección contra caídas II
Notes: 1926.503(a)Training program.
1926.503(a)(1)The employer shall provide a training program for each employee who might be exposed to fall hazards. The program shall enable each employee to recognize the hazards of falling and shall train each employee in the procedures to be followed in order to minimize these hazards.
1926.503(a)(2)The employer shall assure that each employee has been trained, as necessary, by a competent person qualified in the following areas:
1926.503(a)(2)(i)The nature of fall hazards in the work area;
1926.503(a)(2)(ii)The correct procedures for erecting, maintaining, disassembling, and inspecting the fall protection systems to be used;
1926.503(a)(2)(iii)The use and operation of guardrail systems, personal fall arrest systems, safety net systems, warning line systems, safety monitoring systems, controlled access zones, and other protection to be used;
1926.503(a)(2)(iv)The role of each employee in the safety monitoring system when this system is used;
1926.503(a)(2)(v)The limitations on the use of mechanical equipment during the performance of roofing work on low-sloped roofs;
1926.503(a)(2)(vi)The correct procedures for the handling and storage of equipment and materials and the erection of overhead protection; and
1926.503(a)(2)(vii)The role of employees in fall protection plans;
1926.503(a)(2)(viii)The standards contained in this subpart.
1926.503(b)Certification of training.
1926.503(b)(1)The employer shall verify compliance with paragraph (a) of this section by preparing a written certification record. The written certification record shall contain the name or other identity of the employee trained, the date(s) of the training, and the signature of the person who conducted the training or the signature of the employer. If the employer relies on training conducted by another employer or completed prior to the effective date of this section, the certification record shall indicate the date the employer determined the prior training was adequate rather than the date of actual training.
1926.503(b)(2)The latest training certification shall be maintained.
1926.503(c)Retraining. When the employer has reason to believe that any affected employee who has already been trained does not have the understanding and skill required by paragraph (a) of this section, the employer shall retrain each such employee. Circumstances where retraining is required include, but are not limited to, situations where:
1926.503(c)(1)Changes in the workplace render previous training obsolete; or
1926.503(c)(2)Changes in the types of fall protection systems or equipment to be used render previous training obsolete; or
1926.503(c)(3)Inadequacies in an affected employee's knowledge or use of fall protection systems or equipment indicate that the employee has not retained the requisite understanding or skill.
Note: The following appendices to subpart M of this part serve as non-mandatory guidelines to assist employers in complying with the appropriate requirements of subpart M of this part.
[59 FR 40738, Aug. 9, 1994; 60 FR 5131, Jan. 26, 1995]

## Slide 35: Requisitos de capacitación de protección contra caídas 2
El empleador se asegurará de que cada empleado haya sido capacitado, según sea necesario, por una persona competente y calificada en las siguientes áreas:
    La naturaleza de los riesgos de caída en el área de trabajo.
    Los procedimientos correctos para los sistemas de protección contra caídas que deben utilizarse.
    El papel de cada empleado en el sistema de control de seguridad cuando se utilice este sistema.
    Las limitaciones en el uso de equipos mecánicos durante la realización de trabajos en techos de pendiente baja.
Sistemas de protección contra caídas II
Notes: 1926.503(a)Training program.
1926.503(a)(1)The employer shall provide a training program for each employee who might be exposed to fall hazards. The program shall enable each employee to recognize the hazards of falling and shall train each employee in the procedures to be followed in order to minimize these hazards.
1926.503(a)(2)The employer shall assure that each employee has been trained, as necessary, by a competent person qualified in the following areas:
1926.503(a)(2)(i)The nature of fall hazards in the work area;
1926.503(a)(2)(ii)The correct procedures for erecting, maintaining, disassembling, and inspecting the fall protection systems to be used;
1926.503(a)(2)(iii)The use and operation of guardrail systems, personal fall arrest systems, safety net systems, warning line systems, safety monitoring systems, controlled access zones, and other protection to be used;
1926.503(a)(2)(iv)The role of each employee in the safety monitoring system when this system is used;
1926.503(a)(2)(v)The limitations on the use of mechanical equipment during the performance of roofing work on low-sloped roofs;
1926.503(a)(2)(vi)The correct procedures for the handling and storage of equipment and materials and the erection of overhead protection; and
1926.503(a)(2)(vii)The role of employees in fall protection plans;
1926.503(a)(2)(viii)The standards contained in this subpart.
1926.503(b)Certification of training.
1926.503(b)(1)The employer shall verify compliance with paragraph (a) of this section by preparing a written certification record. The written certification record shall contain the name or other identity of the employee trained, the date(s) of the training, and the signature of the person who conducted the training or the signature of the employer. If the employer relies on training conducted by another employer or completed prior to the effective date of this section, the certification record shall indicate the date the employer determined the prior training was adequate rather than the date of actual training.
1926.503(b)(2)The latest training certification shall be maintained.
1926.503(c)Retraining. When the employer has reason to believe that any affected employee who has already been trained does not have the understanding and skill required by paragraph (a) of this section, the employer shall retrain each such employee. Circumstances where retraining is required include, but are not limited to, situations where:
1926.503(c)(1)Changes in the workplace render previous training obsolete; or
1926.503(c)(2)Changes in the types of fall protection systems or equipment to be used render previous training obsolete; or
1926.503(c)(3)Inadequacies in an affected employee's knowledge or use of fall protection systems or equipment indicate that the employee has not retained the requisite understanding or skill.
Note: The following appendices to subpart M of this part serve as non-mandatory guidelines to assist employers in complying with the appropriate requirements of subpart M of this part.
[59 FR 40738, Aug. 9, 1994; 60 FR 5131, Jan. 26, 1995]

## Slide 36: Requisitos de capacitación de protección contra caídas 3
El empleador se asegurará de que cada empleado haya sido capacitado, según sea necesario, por una persona competente y calificada en las siguientes áreas:
    Los procedimientos correctos para manipular y almacenar equipos y materiales, y la instalación de protecciones en altura.
    El papel de los empleados en los planes de protección contra caídas.
Sistemas de protección contra caídas II
Notes: 1926.503(a)Training program.
1926.503(a)(1)The employer shall provide a training program for each employee who might be exposed to fall hazards. The program shall enable each employee to recognize the hazards of falling and shall train each employee in the procedures to be followed in order to minimize these hazards.
1926.503(a)(2)The employer shall assure that each employee has been trained, as necessary, by a competent person qualified in the following areas:
1926.503(a)(2)(i)The nature of fall hazards in the work area;
1926.503(a)(2)(ii)The correct procedures for erecting, maintaining, disassembling, and inspecting the fall protection systems to be used;
1926.503(a)(2)(iii)The use and operation of guardrail systems, personal fall arrest systems, safety net systems, warning line systems, safety monitoring systems, controlled access zones, and other protection to be used;
1926.503(a)(2)(iv)The role of each employee in the safety monitoring system when this system is used;
1926.503(a)(2)(v)The limitations on the use of mechanical equipment during the performance of roofing work on low-sloped roofs;
1926.503(a)(2)(vi)The correct procedures for the handling and storage of equipment and materials and the erection of overhead protection; and
1926.503(a)(2)(vii)The role of employees in fall protection plans;
1926.503(a)(2)(viii)The standards contained in this subpart.
1926.503(b)Certification of training.
1926.503(b)(1)The employer shall verify compliance with paragraph (a) of this section by preparing a written certification record. The written certification record shall contain the name or other identity of the employee trained, the date(s) of the training, and the signature of the person who conducted the training or the signature of the employer. If the employer relies on training conducted by another employer or completed prior to the effective date of this section, the certification record shall indicate the date the employer determined the prior training was adequate rather than the date of actual training.
1926.503(b)(2)The latest training certification shall be maintained.
1926.503(c)Retraining. When the employer has reason to believe that any affected employee who has already been trained does not have the understanding and skill required by paragraph (a) of this section, the employer shall retrain each such employee. Circumstances where retraining is required include, but are not limited to, situations where:
1926.503(c)(1)Changes in the workplace render previous training obsolete; or
1926.503(c)(2)Changes in the types of fall protection systems or equipment to be used render previous training obsolete; or
1926.503(c)(3)Inadequacies in an affected employee's knowledge or use of fall protection systems or equipment indicate that the employee has not retained the requisite understanding or skill.
Note: The following appendices to subpart M of this part serve as non-mandatory guidelines to assist employers in complying with the appropriate requirements of subpart M of this part.
[59 FR 40738, Aug. 9, 1994; 60 FR 5131, Jan. 26, 1995]

## Slide 37: Requisitos de capacitación de protección contra caídas 4
Certificación de capacitación
    El empleador verificará el cumplimiento del párrafo (a) de esta sección mediante la preparación de un registro de certificación por escrito.
    El registro de certificación por escrito deberá contener lo siguiente:
      Nombre u otra identidad del empleado capacitado.
      Fecha/s de la capacitación.
      Firma de la persona que impartió la capacitación o la firma del empleador.
Sistemas de protección contra caídas II
Notes: 1926.503(a)Training program.
1926.503(a)(1)The employer shall provide a training program for each employee who might be exposed to fall hazards. The program shall enable each employee to recognize the hazards of falling and shall train each employee in the procedures to be followed in order to minimize these hazards.
1926.503(a)(2)The employer shall assure that each employee has been trained, as necessary, by a competent person qualified in the following areas:
1926.503(a)(2)(i)The nature of fall hazards in the work area;
1926.503(a)(2)(ii)The correct procedures for erecting, maintaining, disassembling, and inspecting the fall protection systems to be used;
1926.503(a)(2)(iii)The use and operation of guardrail systems, personal fall arrest systems, safety net systems, warning line systems, safety monitoring systems, controlled access zones, and other protection to be used;
1926.503(a)(2)(iv)The role of each employee in the safety monitoring system when this system is used;
1926.503(a)(2)(v)The limitations on the use of mechanical equipment during the performance of roofing work on low-sloped roofs;
1926.503(a)(2)(vi)The correct procedures for the handling and storage of equipment and materials and the erection of overhead protection; and
1926.503(a)(2)(vii)The role of employees in fall protection plans;
1926.503(a)(2)(viii)The standards contained in this subpart.
1926.503(b)Certification of training.
1926.503(b)(1)The employer shall verify compliance with paragraph (a) of this section by preparing a written certification record. The written certification record shall contain the name or other identity of the employee trained, the date(s) of the training, and the signature of the person who conducted the training or the signature of the employer. If the employer relies on training conducted by another employer or completed prior to the effective date of this section, the certification record shall indicate the date the employer determined the prior training was adequate rather than the date of actual training.
1926.503(b)(2)The latest training certification shall be maintained.
1926.503(c)Retraining. When the employer has reason to believe that any affected employee who has already been trained does not have the understanding and skill required by paragraph (a) of this section, the employer shall retrain each such employee. Circumstances where retraining is required include, but are not limited to, situations where:
1926.503(c)(1)Changes in the workplace render previous training obsolete; or
1926.503(c)(2)Changes in the types of fall protection systems or equipment to be used render previous training obsolete; or
1926.503(c)(3)Inadequacies in an affected employee's knowledge or use of fall protection systems or equipment indicate that the employee has not retained the requisite understanding or skill.
Note: The following appendices to subpart M of this part serve as non-mandatory guidelines to assist employers in complying with the appropriate requirements of subpart M of this part.
[59 FR 40738, Aug. 9, 1994; 60 FR 5131, Jan. 26, 1995]

## Slide 38: Requisitos de capacitación de protección contra caídas 5
Certificación de capacitación
    Si el empleador se basa en la capacitación realizada por otro empleador o completada antes de la fecha de entrada en vigor de esta sección, el registro de certificación deberá indicar la fecha en que el empleador determinó que la capacitación anterior era adecuada en lugar de la fecha de la capacitación actual.
    Deberá conservarse el último certificado de capacitación.
Sistemas de protección contra caídas II
Notes: 1926.503(a)Training program.
1926.503(a)(1)The employer shall provide a training program for each employee who might be exposed to fall hazards. The program shall enable each employee to recognize the hazards of falling and shall train each employee in the procedures to be followed in order to minimize these hazards.
1926.503(a)(2)The employer shall assure that each employee has been trained, as necessary, by a competent person qualified in the following areas:
1926.503(a)(2)(i)The nature of fall hazards in the work area;
1926.503(a)(2)(ii)The correct procedures for erecting, maintaining, disassembling, and inspecting the fall protection systems to be used;
1926.503(a)(2)(iii)The use and operation of guardrail systems, personal fall arrest systems, safety net systems, warning line systems, safety monitoring systems, controlled access zones, and other protection to be used;
1926.503(a)(2)(iv)The role of each employee in the safety monitoring system when this system is used;
1926.503(a)(2)(v)The limitations on the use of mechanical equipment during the performance of roofing work on low-sloped roofs;
1926.503(a)(2)(vi)The correct procedures for the handling and storage of equipment and materials and the erection of overhead protection; and
1926.503(a)(2)(vii)The role of employees in fall protection plans;
1926.503(a)(2)(viii)The standards contained in this subpart.
1926.503(b)Certification of training.
1926.503(b)(1)The employer shall verify compliance with paragraph (a) of this section by preparing a written certification record. The written certification record shall contain the name or other identity of the employee trained, the date(s) of the training, and the signature of the person who conducted the training or the signature of the employer. If the employer relies on training conducted by another employer or completed prior to the effective date of this section, the certification record shall indicate the date the employer determined the prior training was adequate rather than the date of actual training.
1926.503(b)(2)The latest training certification shall be maintained.
1926.503(c)Retraining. When the employer has reason to believe that any affected employee who has already been trained does not have the understanding and skill required by paragraph (a) of this section, the employer shall retrain each such employee. Circumstances where retraining is required include, but are not limited to, situations where:
1926.503(c)(1)Changes in the workplace render previous training obsolete; or
1926.503(c)(2)Changes in the types of fall protection systems or equipment to be used render previous training obsolete; or
1926.503(c)(3)Inadequacies in an affected employee's knowledge or use of fall protection systems or equipment indicate that the employee has not retained the requisite understanding or skill.
Note: The following appendices to subpart M of this part serve as non-mandatory guidelines to assist employers in complying with the appropriate requirements of subpart M of this part.
[59 FR 40738, Aug. 9, 1994; 60 FR 5131, Jan. 26, 1995]

## Slide 39: Requisitos de capacitación de protección contra caídas 6
Cuando el empleador tenga motivos para creer que cualquier empleado afectado que ya haya recibido capacitación no posee la comprensión y la habilidad requeridas, deberá volver a capacitar a cada uno de dichos empleados.
Las circunstancias en las que se requiere una nueva capacitación incluyen, entre otras, las siguientes:
    Cambios en el lugar de trabajo que dejan obsoleta la capacitación anterior.
    Cambios en los tipos de sistemas de protección contra caídas o equipos que se van a utilizar que dejan obsoleta la capacitación anterior.
    Insuficiencias en los conocimientos de un empleado afectado o en el uso de los sistemas o equipos de protección contra caídas que indican que el empleado no ha conservado la comprensión ni habilidad requeridas.
Sistemas de protección contra caídas II
Notes: 1926.503(a)Training program.
1926.503(a)(1)The employer shall provide a training program for each employee who might be exposed to fall hazards. The program shall enable each employee to recognize the hazards of falling and shall train each employee in the procedures to be followed in order to minimize these hazards.
1926.503(a)(2)The employer shall assure that each employee has been trained, as necessary, by a competent person qualified in the following areas:
1926.503(a)(2)(i)The nature of fall hazards in the work area;
1926.503(a)(2)(ii)The correct procedures for erecting, maintaining, disassembling, and inspecting the fall protection systems to be used;
1926.503(a)(2)(iii)The use and operation of guardrail systems, personal fall arrest systems, safety net systems, warning line systems, safety monitoring systems, controlled access zones, and other protection to be used;
1926.503(a)(2)(iv)The role of each employee in the safety monitoring system when this system is used;
1926.503(a)(2)(v)The limitations on the use of mechanical equipment during the performance of roofing work on low-sloped roofs;
1926.503(a)(2)(vi)The correct procedures for the handling and storage of equipment and materials and the erection of overhead protection; and
1926.503(a)(2)(vii)The role of employees in fall protection plans;
1926.503(a)(2)(viii)The standards contained in this subpart.
1926.503(b)Certification of training.
1926.503(b)(1)The employer shall verify compliance with paragraph (a) of this section by preparing a written certification record. The written certification record shall contain the name or other identity of the employee trained, the date(s) of the training, and the signature of the person who conducted the training or the signature of the employer. If the employer relies on training conducted by another employer or completed prior to the effective date of this section, the certification record shall indicate the date the employer determined the prior training was adequate rather than the date of actual training.
1926.503(b)(2)The latest training certification shall be maintained.
1926.503(c)Retraining. When the employer has reason to believe that any affected employee who has already been trained does not have the understanding and skill required by paragraph (a) of this section, the employer shall retrain each such employee. Circumstances where retraining is required include, but are not limited to, situations where:
1926.503(c)(1)Changes in the workplace render previous training obsolete; or
1926.503(c)(2)Changes in the types of fall protection systems or equipment to be used render previous training obsolete; or
1926.503(c)(3)Inadequacies in an affected employee's knowledge or use of fall protection systems or equipment indicate that the employee has not retained the requisite understanding or skill.
Note: The following appendices to subpart M of this part serve as non-mandatory guidelines to assist employers in complying with the appropriate requirements of subpart M of this part.
[59 FR 40738, Aug. 9, 1994; 60 FR 5131, Jan. 26, 1995]

## Slide 40: ¿Tiene preguntas?
Sistemas de protección contra caídas II