## Slide 1: Sistemas de protección contra caídas I
Prevención de caídas en la construcción
Criterios y prácticas

## Slide 2: Objetivos de aprendizaje
Comprensión de las prácticas recomendadas básicas asociadas con los sistemas de protección contra caídas siguientes:
    Barandas
    Sistemas personales de detención de caídas (Personal Fall Arrest Systems, PFAS)
    Redes de seguridad
Sistemas de protección contra caídas I

## Slide 3: ¿Realmente necesito protección contra caídas?
He pensado cuidadosamente todos los aspectos.
Nada podría salir mal y, de todos modos, no me sucedería a mí.
Lo he hecho miles de veces.
Sé lo que estoy haciendo, es para lo que me he capacitado toda la vida.
Sistemas de protección contra caídas I

## Slide 4: Sistemas de protección contra caídas 1
Sistemas de barandas
Sistemas de redes de seguridad
Sistemas personales de detención de caídas (PFAS)
Sistemas de dispositivos de posicionamiento
Sistemas de líneas de advertencia
Sistemas de protección contra caídas I

## Slide 5: Sistemas de protección contra caídas 2
Zonas de acceso controlado
Sistemas de control de seguridad
Cubiertas
Protección contra caída de objetos
Plan de protección contra caídas
Sistemas de protección contra caídas I

## Slide 6: Sistemas de barandas 1
Postes: 8 pies de distancia.
Barandas superiores: 42 pulgadas + 3 pulgadas, capaz de soportar 200 libras de fuerza.
Largueros intermedios: a medio camino entre la baranda superior y la superficie de trabajo, y capaz de soportar 150 libras de fuerza.
Tabla de capellada: 3 ½ pulgadas de alto, clavados en el lugar e instalados a ras con la superficie de trabajo.
Sistemas de protección contra caídas I
Notes: 1926.502(b)"Guardrail systems." Guardrail systems and their use shall comply with the following provisions:
1926.502(b)(1)Top edge height of top rails, or equivalent guardrail system members, shall be 42 inches (1.1 m) plus or minus 3 inches (8 cm) above the walking/working level. When conditions warrant, the height of the top edge may exceed the 45-inch height, provided the guardrail system meets all other criteria of this paragraph.
Note: When employees are using stilts, the top edge height of the top rail, or equivalent member, shall be increased an amount equal to the height of the stilts.
1926.502(b)(2)Midrails, screens, mesh, intermediate vertical members, or equivalent intermediate structural members shall be installed between the top edge of the guardrail system and the walking/working surface when there is no wall or parapet wall at least 21 inches (53 cm) high.
1926.502(b)(2)(i)Midrails, when used, shall be installed at a height midway between the top edge of the guardrail system and the walking/working level.
1926.502(b)(2)(ii)Screens and mesh, when used, shall extend from the top rail to the walking/working level and along the entire opening between top rail supports.
1926.502(b)(2)(iii)Intermediate members (such as balusters), when used between posts, shall be not more than 19 inches (48 cm) apart.
1926.502(b)(2)(iv)Other structural members (such as additional midrails and architectural panels) shall be installed such that there are no openings in the guardrail system that are more than 19 inches (.5 m) wide.
1926.502(b)(3)Guardrail systems shall be capable of withstanding, without failure, a force of at least 200 pounds (890 N) applied within 2 inches (5.1 cm) of the top edge, in any outward or downward direction, at any point along the top edge.
1926.502(b)(4)When the 200 pound (890 N) test load specified in paragraph (b)(3) of this section is applied in a downward direction, the top edge of the guardrail shall not deflect to a height less than 39 inches (1.0 m) above the walking/working level. Guardrail system components selected and constructed in accordance with the Appendix B to subpart M of this part will be deemed to meet this requirement.
1926.502(b)(5)Midrails, screens, mesh, intermediate vertical members, solid panels, and equivalent structural members shall be capable of withstanding, without failure, a force of at least 150 pounds (666 N) applied in any downward or outward direction at any point along the midrail or other member.
1926.502(b)(6)Guardrail systems shall be so surfaced as to prevent injury to an employee from punctures or lacerations, and to prevent snagging of clothing.
1926.502(b)(7)The ends of all top rails and midrails shall not overhang the terminal posts, except where such overhang does not constitute a projection hazard.
1926.502(b)(8)Steel banding and plastic banding shall not be used as top rails or midrails.
1926.502(b)(9)Top rails and midrails shall be at least one-quarter inch (0.6 cm) nominal diameter or thickness to prevent cuts and lacerations. If wire rope is used for top rails, it shall be flagged at not more than 6-foot intervals with high-visibility material.
1926.502(b)(10)When guardrail systems are used at hoisting areas, a chain, gate or removable guardrail section shall be placed across the access opening between guardrail sections when hoisting operations are not taking place.
1926.502(b)(11)When guardrail systems are used at holes, they shall be erected on all unprotected sides or edges of the hole.
1926.502(b)(12)When guardrail systems are used around holes used for the passage of materials, the hole shall have not more than two sides provided with removable guardrail sections to allow the passage of materials. When the hole is not in use, it shall be closed over with a cover, or a guardrail system shall be provided along all unprotected sides or edges.
1926.502(b)(13)When guardrail systems are used around holes which are used as points of access (such as ladderways), they shall be provided with a gate, or be so offset that a person cannot walk directly into the hole.
1926.502(b)(14)Guardrail systems used on ramps and runways shall be erected along each unprotected side or edge.
1926.502(b)(15)Manila, plastic or synthetic rope being used for top rails or midrails shall be inspected as frequently as necessary to ensure that it continues to meet the strength requirements of paragraph (b)(3) of this section.

## Slide 7: Sistemas de barandas 2
Cuando se utilicen elementos intermedios (como balaustres) entre postes, no deben estar separados a más de 19 pulgadas.
    Otros elementos estructurales (como largueros intermedios y paneles arquitectónicos adicionales) deben instalarse de manera que no haya aberturas en el sistemas de barandas de más de 19 pulgadas de ancho.
Cuando se utilicen pantallas y mallas, estas deben extenderse desde la baranda superior hasta el nivel de paso o de trabajo y a lo largo de toda la abertura entre los soportes de la baranda superior.
Los sistemas de barandas deben tener una superficie que proteja a los trabajadores de pinchazos o cortes y que evite que la vestimenta se enganche.
Sistemas de protección contra caídas I
Notes: 1926.502(b)"Guardrail systems." Guardrail systems and their use shall comply with the following provisions:
1926.502(b)(1)Top edge height of top rails, or equivalent guardrail system members, shall be 42 inches (1.1 m) plus or minus 3 inches (8 cm) above the walking/working level. When conditions warrant, the height of the top edge may exceed the 45-inch height, provided the guardrail system meets all other criteria of this paragraph.
Note: When employees are using stilts, the top edge height of the top rail, or equivalent member, shall be increased an amount equal to the height of the stilts.
1926.502(b)(2)Midrails, screens, mesh, intermediate vertical members, or equivalent intermediate structural members shall be installed between the top edge of the guardrail system and the walking/working surface when there is no wall or parapet wall at least 21 inches (53 cm) high.
1926.502(b)(2)(i)Midrails, when used, shall be installed at a height midway between the top edge of the guardrail system and the walking/working level.
1926.502(b)(2)(ii)Screens and mesh, when used, shall extend from the top rail to the walking/working level and along the entire opening between top rail supports.
1926.502(b)(2)(iii)Intermediate members (such as balusters), when used between posts, shall be not more than 19 inches (48 cm) apart.
1926.502(b)(2)(iv)Other structural members (such as additional midrails and architectural panels) shall be installed such that there are no openings in the guardrail system that are more than 19 inches (.5 m) wide.
1926.502(b)(3)Guardrail systems shall be capable of withstanding, without failure, a force of at least 200 pounds (890 N) applied within 2 inches (5.1 cm) of the top edge, in any outward or downward direction, at any point along the top edge.
1926.502(b)(4)When the 200 pound (890 N) test load specified in paragraph (b)(3) of this section is applied in a downward direction, the top edge of the guardrail shall not deflect to a height less than 39 inches (1.0 m) above the walking/working level. Guardrail system components selected and constructed in accordance with the Appendix B to subpart M of this part will be deemed to meet this requirement.
1926.502(b)(5)Midrails, screens, mesh, intermediate vertical members, solid panels, and equivalent structural members shall be capable of withstanding, without failure, a force of at least 150 pounds (666 N) applied in any downward or outward direction at any point along the midrail or other member.
1926.502(b)(6)Guardrail systems shall be so surfaced as to prevent injury to an employee from punctures or lacerations, and to prevent snagging of clothing.
1926.502(b)(7)The ends of all top rails and midrails shall not overhang the terminal posts, except where such overhang does not constitute a projection hazard.
1926.502(b)(8)Steel banding and plastic banding shall not be used as top rails or midrails.
1926.502(b)(9)Top rails and midrails shall be at least one-quarter inch (0.6 cm) nominal diameter or thickness to prevent cuts and lacerations. If wire rope is used for top rails, it shall be flagged at not more than 6-foot intervals with high-visibility material.
1926.502(b)(10)When guardrail systems are used at hoisting areas, a chain, gate or removable guardrail section shall be placed across the access opening between guardrail sections when hoisting operations are not taking place.
1926.502(b)(11)When guardrail systems are used at holes, they shall be erected on all unprotected sides or edges of the hole.
1926.502(b)(12)When guardrail systems are used around holes used for the passage of materials, the hole shall have not more than two sides provided with removable guardrail sections to allow the passage of materials. When the hole is not in use, it shall be closed over with a cover, or a guardrail system shall be provided along all unprotected sides or edges.
1926.502(b)(13)When guardrail systems are used around holes which are used as points of access (such as ladderways), they shall be provided with a gate, or be so offset that a person cannot walk directly into the hole.
1926.502(b)(14)Guardrail systems used on ramps and runways shall be erected along each unprotected side or edge.
1926.502(b)(15)Manila, plastic or synthetic rope being used for top rails or midrails shall be inspected as frequently as necessary to ensure that it continues to meet the strength requirements of paragraph (b)(3) of this section.

## Slide 8: Sistemas de barandas 3
Las barandas superiores y los largueros intermedios de los sistemas de barandas deben tener un diámetro nominal o un grosor de al menos 14 pulgadas para evitar cortes y laceraciones.
    Barandas superiores: 42 pulgadas + 3 pulgadas.
    Largueros intermedios: a medio camino entre la baranda superior y la superficie de trabajo, y capaz de soportar 150 libras de fuerza.
Si se utiliza un cable metálico para las barandas superiores, deberá señalizarse a intervalos de no más de 6 pies con material de alta visibilidad.
Si se utilizan sistemas de barandas alrededor de huecos que se utilizan como puntos de acceso (como pasarelas), deben utilizarse puertas. Otra posibilidad es desplazar el punto de acceso para evitar que los trabajadores entren accidentalmente en el hueco.
Sistemas de protección contra caídas I
Notes: 1926.502(b)"Guardrail systems." Guardrail systems and their use shall comply with the following provisions:
1926.502(b)(1)Top edge height of top rails, or equivalent guardrail system members, shall be 42 inches (1.1 m) plus or minus 3 inches (8 cm) above the walking/working level. When conditions warrant, the height of the top edge may exceed the 45-inch height, provided the guardrail system meets all other criteria of this paragraph.
Note: When employees are using stilts, the top edge height of the top rail, or equivalent member, shall be increased an amount equal to the height of the stilts.
1926.502(b)(2)Midrails, screens, mesh, intermediate vertical members, or equivalent intermediate structural members shall be installed between the top edge of the guardrail system and the walking/working surface when there is no wall or parapet wall at least 21 inches (53 cm) high.
1926.502(b)(2)(i)Midrails, when used, shall be installed at a height midway between the top edge of the guardrail system and the walking/working level.
1926.502(b)(2)(ii)Screens and mesh, when used, shall extend from the top rail to the walking/working level and along the entire opening between top rail supports.
1926.502(b)(2)(iii)Intermediate members (such as balusters), when used between posts, shall be not more than 19 inches (48 cm) apart.
1926.502(b)(2)(iv)Other structural members (such as additional midrails and architectural panels) shall be installed such that there are no openings in the guardrail system that are more than 19 inches (.5 m) wide.
1926.502(b)(3)Guardrail systems shall be capable of withstanding, without failure, a force of at least 200 pounds (890 N) applied within 2 inches (5.1 cm) of the top edge, in any outward or downward direction, at any point along the top edge.
1926.502(b)(4)When the 200 pound (890 N) test load specified in paragraph (b)(3) of this section is applied in a downward direction, the top edge of the guardrail shall not deflect to a height less than 39 inches (1.0 m) above the walking/working level. Guardrail system components selected and constructed in accordance with the Appendix B to subpart M of this part will be deemed to meet this requirement.
1926.502(b)(5)Midrails, screens, mesh, intermediate vertical members, solid panels, and equivalent structural members shall be capable of withstanding, without failure, a force of at least 150 pounds (666 N) applied in any downward or outward direction at any point along the midrail or other member.
1926.502(b)(6)Guardrail systems shall be so surfaced as to prevent injury to an employee from punctures or lacerations, and to prevent snagging of clothing.
1926.502(b)(7)The ends of all top rails and midrails shall not overhang the terminal posts, except where such overhang does not constitute a projection hazard.
1926.502(b)(8)Steel banding and plastic banding shall not be used as top rails or midrails.
1926.502(b)(9)Top rails and midrails shall be at least one-quarter inch (0.6 cm) nominal diameter or thickness to prevent cuts and lacerations. If wire rope is used for top rails, it shall be flagged at not more than 6-foot intervals with high-visibility material.
1926.502(b)(10)When guardrail systems are used at hoisting areas, a chain, gate or removable guardrail section shall be placed across the access opening between guardrail sections when hoisting operations are not taking place.
1926.502(b)(11)When guardrail systems are used at holes, they shall be erected on all unprotected sides or edges of the hole.
1926.502(b)(12)When guardrail systems are used around holes used for the passage of materials, the hole shall have not more than two sides provided with removable guardrail sections to allow the passage of materials. When the hole is not in use, it shall be closed over with a cover, or a guardrail system shall be provided along all unprotected sides or edges.
1926.502(b)(13)When guardrail systems are used around holes which are used as points of access (such as ladderways), they shall be provided with a gate, or be so offset that a person cannot walk directly into the hole.
1926.502(b)(14)Guardrail systems used on ramps and runways shall be erected along each unprotected side or edge.
1926.502(b)(15)Manila, plastic or synthetic rope being used for top rails or midrails shall be inspected as frequently as necessary to ensure that it continues to meet the strength requirements of paragraph (b)(3) of this section.

## Slide 9: Sistemas de barandas 4
Sistemas de protección contra caídas I
Notes: 1926.502(b)"Guardrail systems." Guardrail systems and their use shall comply with the following provisions:
1926.502(b)(1)Top edge height of top rails, or equivalent guardrail system members, shall be 42 inches (1.1 m) plus or minus 3 inches (8 cm) above the walking/working level. When conditions warrant, the height of the top edge may exceed the 45-inch height, provided the guardrail system meets all other criteria of this paragraph.
Note: When employees are using stilts, the top edge height of the top rail, or equivalent member, shall be increased an amount equal to the height of the stilts.
1926.502(b)(2)Midrails, screens, mesh, intermediate vertical members, or equivalent intermediate structural members shall be installed between the top edge of the guardrail system and the walking/working surface when there is no wall or parapet wall at least 21 inches (53 cm) high.
1926.502(b)(2)(i)Midrails, when used, shall be installed at a height midway between the top edge of the guardrail system and the walking/working level.
1926.502(b)(2)(ii)Screens and mesh, when used, shall extend from the top rail to the walking/working level and along the entire opening between top rail supports.
1926.502(b)(2)(iii)Intermediate members (such as balusters), when used between posts, shall be not more than 19 inches (48 cm) apart.
1926.502(b)(2)(iv)Other structural members (such as additional midrails and architectural panels) shall be installed such that there are no openings in the guardrail system that are more than 19 inches (.5 m) wide.
1926.502(b)(3)Guardrail systems shall be capable of withstanding, without failure, a force of at least 200 pounds (890 N) applied within 2 inches (5.1 cm) of the top edge, in any outward or downward direction, at any point along the top edge.
1926.502(b)(4)When the 200 pound (890 N) test load specified in paragraph (b)(3) of this section is applied in a downward direction, the top edge of the guardrail shall not deflect to a height less than 39 inches (1.0 m) above the walking/working level. Guardrail system components selected and constructed in accordance with the Appendix B to subpart M of this part will be deemed to meet this requirement.
1926.502(b)(5)Midrails, screens, mesh, intermediate vertical members, solid panels, and equivalent structural members shall be capable of withstanding, without failure, a force of at least 150 pounds (666 N) applied in any downward or outward direction at any point along the midrail or other member.
1926.502(b)(6)Guardrail systems shall be so surfaced as to prevent injury to an employee from punctures or lacerations, and to prevent snagging of clothing.
1926.502(b)(7)The ends of all top rails and midrails shall not overhang the terminal posts, except where such overhang does not constitute a projection hazard.
1926.502(b)(8)Steel banding and plastic banding shall not be used as top rails or midrails.
1926.502(b)(9)Top rails and midrails shall be at least one-quarter inch (0.6 cm) nominal diameter or thickness to prevent cuts and lacerations. If wire rope is used for top rails, it shall be flagged at not more than 6-foot intervals with high-visibility material.
1926.502(b)(10)When guardrail systems are used at hoisting areas, a chain, gate or removable guardrail section shall be placed across the access opening between guardrail sections when hoisting operations are not taking place.
1926.502(b)(11)When guardrail systems are used at holes, they shall be erected on all unprotected sides or edges of the hole.
1926.502(b)(12)When guardrail systems are used around holes used for the passage of materials, the hole shall have not more than two sides provided with removable guardrail sections to allow the passage of materials. When the hole is not in use, it shall be closed over with a cover, or a guardrail system shall be provided along all unprotected sides or edges.
1926.502(b)(13)When guardrail systems are used around holes which are used as points of access (such as ladderways), they shall be provided with a gate, or be so offset that a person cannot walk directly into the hole.
1926.502(b)(14)Guardrail systems used on ramps and runways shall be erected along each unprotected side or edge.
1926.502(b)(15)Manila, plastic or synthetic rope being used for top rails or midrails shall be inspected as frequently as necessary to ensure that it continues to meet the strength requirements of paragraph (b)(3) of this section.

## Slide 10: Sistemas de barandas 5
Tubería de 1 ½” de diámetro exterior
Ángulos de 2” x 2” x ¼”
Estándar 2” x 4”
Cable (mínimo de ¼”)
Sistemas de protección contra caídas I
Notes: 1926.502(b)"Guardrail systems." Guardrail systems and their use shall comply with the following provisions:
1926.502(b)(1)Top edge height of top rails, or equivalent guardrail system members, shall be 42 inches (1.1 m) plus or minus 3 inches (8 cm) above the walking/working level. When conditions warrant, the height of the top edge may exceed the 45-inch height, provided the guardrail system meets all other criteria of this paragraph.
Note: When employees are using stilts, the top edge height of the top rail, or equivalent member, shall be increased an amount equal to the height of the stilts.
1926.502(b)(2)Midrails, screens, mesh, intermediate vertical members, or equivalent intermediate structural members shall be installed between the top edge of the guardrail system and the walking/working surface when there is no wall or parapet wall at least 21 inches (53 cm) high.
1926.502(b)(2)(i)Midrails, when used, shall be installed at a height midway between the top edge of the guardrail system and the walking/working level.
1926.502(b)(2)(ii)Screens and mesh, when used, shall extend from the top rail to the walking/working level and along the entire opening between top rail supports.
1926.502(b)(2)(iii)Intermediate members (such as balusters), when used between posts, shall be not more than 19 inches (48 cm) apart.
1926.502(b)(2)(iv)Other structural members (such as additional midrails and architectural panels) shall be installed such that there are no openings in the guardrail system that are more than 19 inches (.5 m) wide.
1926.502(b)(3)Guardrail systems shall be capable of withstanding, without failure, a force of at least 200 pounds (890 N) applied within 2 inches (5.1 cm) of the top edge, in any outward or downward direction, at any point along the top edge.
1926.502(b)(4)When the 200 pound (890 N) test load specified in paragraph (b)(3) of this section is applied in a downward direction, the top edge of the guardrail shall not deflect to a height less than 39 inches (1.0 m) above the walking/working level. Guardrail system components selected and constructed in accordance with the Appendix B to subpart M of this part will be deemed to meet this requirement.
1926.502(b)(5)Midrails, screens, mesh, intermediate vertical members, solid panels, and equivalent structural members shall be capable of withstanding, without failure, a force of at least 150 pounds (666 N) applied in any downward or outward direction at any point along the midrail or other member.
1926.502(b)(6)Guardrail systems shall be so surfaced as to prevent injury to an employee from punctures or lacerations, and to prevent snagging of clothing.
1926.502(b)(7)The ends of all top rails and midrails shall not overhang the terminal posts, except where such overhang does not constitute a projection hazard.
1926.502(b)(8)Steel banding and plastic banding shall not be used as top rails or midrails.
1926.502(b)(9)Top rails and midrails shall be at least one-quarter inch (0.6 cm) nominal diameter or thickness to prevent cuts and lacerations. If wire rope is used for top rails, it shall be flagged at not more than 6-foot intervals with high-visibility material.
1926.502(b)(10)When guardrail systems are used at hoisting areas, a chain, gate or removable guardrail section shall be placed across the access opening between guardrail sections when hoisting operations are not taking place.
1926.502(b)(11)When guardrail systems are used at holes, they shall be erected on all unprotected sides or edges of the hole.
1926.502(b)(12)When guardrail systems are used around holes used for the passage of materials, the hole shall have not more than two sides provided with removable guardrail sections to allow the passage of materials. When the hole is not in use, it shall be closed over with a cover, or a guardrail system shall be provided along all unprotected sides or edges.
1926.502(b)(13)When guardrail systems are used around holes which are used as points of access (such as ladderways), they shall be provided with a gate, or be so offset that a person cannot walk directly into the hole.
1926.502(b)(14)Guardrail systems used on ramps and runways shall be erected along each unprotected side or edge.
1926.502(b)(15)Manila, plastic or synthetic rope being used for top rails or midrails shall be inspected as frequently as necessary to ensure that it continues to meet the strength requirements of paragraph (b)(3) of this section.

## Slide 11: Sistemas de barandas 6
Barandas portátiles con peso
Sistemas de protección contra caídas I
Notes: 1926.502(b)"Guardrail systems." Guardrail systems and their use shall comply with the following provisions:
1926.502(b)(1)Top edge height of top rails, or equivalent guardrail system members, shall be 42 inches (1.1 m) plus or minus 3 inches (8 cm) above the walking/working level. When conditions warrant, the height of the top edge may exceed the 45-inch height, provided the guardrail system meets all other criteria of this paragraph. Note: When employees are using stilts, the top edge height of the top rail, or equivalent member, shall be increased an amount equal to the height of the stilts.
1926.502(b)(2)Midrails, screens, mesh, intermediate vertical members, or equivalent intermediate structural members shall be installed between the top edge of the guardrail system and the walking/working surface when there is no wall or parapet wall at least 21 inches (53 cm) high.
1926.502(b)(2)(i)Midrails, when used, shall be installed at a height midway between the top edge of the guardrail system and the walking/working level.
1926.502(b)(2)(ii)Screens and mesh, when used, shall extend from the top rail to the walking/working level and along the entire opening between top rail supports.
1926.502(b)(2)(iii)Intermediate members (such as balusters), when used between posts, shall be not more than 19 inches (48 cm) apart.
1926.502(b)(2)(iv)Other structural members (such as additional midrails and architectural panels) shall be installed such that there are no openings in the guardrail system that are more than 19 inches (.5 m) wide.
1926.502(b)(3)Guardrail systems shall be capable of withstanding, without failure, a force of at least 200 pounds (890 N) applied within 2 inches (5.1 cm) of the top edge, in any outward or downward direction, at any point along the top edge.
1926.502(b)(4)When the 200 pound (890 N) test load specified in paragraph (b)(3) of this section is applied in a downward direction, the top edge of the guardrail shall not deflect to a height less than 39 inches (1.0 m) above the walking/working level. Guardrail system components selected and constructed in accordance with the Appendix B to subpart M of this part will be deemed to meet this requirement.
1926.502(b)(5)Midrails, screens, mesh, intermediate vertical members, solid panels, and equivalent structural members shall be capable of withstanding, without failure, a force of at least 150 pounds (666 N) applied in any downward or outward direction at any point along the midrail or other member.
1926.502(b)(6)Guardrail systems shall be so surfaced as to prevent injury to an employee from punctures or lacerations, and to prevent snagging of clothing.
1926.502(b)(7)The ends of all top rails and midrails shall not overhang the terminal posts, except where such overhang does not constitute a projection hazard.
1926.502(b)(8)Steel banding and plastic banding shall not be used as top rails or midrails.
1926.502(b)(9)Top rails and midrails shall be at least one-quarter inch (0.6 cm) nominal diameter or thickness to prevent cuts and lacerations. If wire rope is used for top rails, it shall be flagged at not more than 6-foot intervals with high-visibility material.
1926.502(b)(10)When guardrail systems are used at hoisting areas, a chain, gate or removable guardrail section shall be placed across the access opening between guardrail sections when hoisting operations are not taking place.
1926.502(b)(11)When guardrail systems are used at holes, they shall be erected on all unprotected sides or edges of the hole.
1926.502(b)(12)When guardrail systems are used around holes used for the passage of materials, the hole shall have not more than two sides provided with removable guardrail sections to allow the passage of materials. When the hole is not in use, it shall be closed over with a cover, or a guardrail system shall be provided along all unprotected sides or edges.
1926.502(b)(13)When guardrail systems are used around holes which are used as points of access (such as ladderways), they shall be provided with a gate, or be so offset that a person cannot walk directly into the hole.
1926.502(b)(14)Guardrail systems used on ramps and runways shall be erected along each unprotected side or edge.
1926.502(b)(15)Manila, plastic or synthetic rope being used for top rails or midrails shall be inspected as frequently as necessary to ensure that it continues to meet the strength requirements of paragraph (b)(3) of this section.

## Slide 12: Sistemas de barandas 7
Cuando los empleados trabajan por encima de las barandas, deben estar protegidos para no caer sobre estas.
Sistemas de protección contra caídas I
Notes: 1926.502(b)"Guardrail systems." Guardrail systems and their use shall comply with the following provisions:
1926.502(b)(1)Top edge height of top rails, or equivalent guardrail system members, shall be 42 inches (1.1 m) plus or minus 3 inches (8 cm) above the walking/working level. When conditions warrant, the height of the top edge may exceed the 45-inch height, provided the guardrail system meets all other criteria of this paragraph. Note: When employees are using stilts, the top edge height of the top rail, or equivalent member, shall be increased an amount equal to the height of the stilts.
1926.502(b)(2)Midrails, screens, mesh, intermediate vertical members, or equivalent intermediate structural members shall be installed between the top edge of the guardrail system and the walking/working surface when there is no wall or parapet wall at least 21 inches (53 cm) high.
1926.502(b)(2)(i)Midrails, when used, shall be installed at a height midway between the top edge of the guardrail system and the walking/working level.
1926.502(b)(2)(ii)Screens and mesh, when used, shall extend from the top rail to the walking/working level and along the entire opening between top rail supports.
1926.502(b)(2)(iii)Intermediate members (such as balusters), when used between posts, shall be not more than 19 inches (48 cm) apart.
1926.502(b)(2)(iv)Other structural members (such as additional midrails and architectural panels) shall be installed such that there are no openings in the guardrail system that are more than 19 inches (.5 m) wide.
1926.502(b)(3)Guardrail systems shall be capable of withstanding, without failure, a force of at least 200 pounds (890 N) applied within 2 inches (5.1 cm) of the top edge, in any outward or downward direction, at any point along the top edge.
1926.502(b)(4)When the 200 pound (890 N) test load specified in paragraph (b)(3) of this section is applied in a downward direction, the top edge of the guardrail shall not deflect to a height less than 39 inches (1.0 m) above the walking/working level. Guardrail system components selected and constructed in accordance with the Appendix B to subpart M of this part will be deemed to meet this requirement.
1926.502(b)(5)Midrails, screens, mesh, intermediate vertical members, solid panels, and equivalent structural members shall be capable of withstanding, without failure, a force of at least 150 pounds (666 N) applied in any downward or outward direction at any point along the midrail or other member.
1926.502(b)(6)Guardrail systems shall be so surfaced as to prevent injury to an employee from punctures or lacerations, and to prevent snagging of clothing.
1926.502(b)(7)The ends of all top rails and midrails shall not overhang the terminal posts, except where such overhang does not constitute a projection hazard.
1926.502(b)(8)Steel banding and plastic banding shall not be used as top rails or midrails.
1926.502(b)(9)Top rails and midrails shall be at least one-quarter inch (0.6 cm) nominal diameter or thickness to prevent cuts and lacerations. If wire rope is used for top rails, it shall be flagged at not more than 6-foot intervals with high-visibility material.
1926.502(b)(10)When guardrail systems are used at hoisting areas, a chain, gate or removable guardrail section shall be placed across the access opening between guardrail sections when hoisting operations are not taking place.
1926.502(b)(11)When guardrail systems are used at holes, they shall be erected on all unprotected sides or edges of the hole.
1926.502(b)(12)When guardrail systems are used around holes used for the passage of materials, the hole shall have not more than two sides provided with removable guardrail sections to allow the passage of materials. When the hole is not in use, it shall be closed over with a cover, or a guardrail system shall be provided along all unprotected sides or edges.
1926.502(b)(13)When guardrail systems are used around holes which are used as points of access (such as ladderways), they shall be provided with a gate, or be so offset that a person cannot walk directly into the hole.
1926.502(b)(14)Guardrail systems used on ramps and runways shall be erected along each unprotected side or edge.
1926.502(b)(15)Manila, plastic or synthetic rope being used for top rails or midrails shall be inspected as frequently as necessary to ensure that it continues to meet the strength requirements of paragraph (b)(3) of this section.

## Slide 13: Sistemas de redes de seguridad 1
Instálelo lo más cerca posible de la superficie de paso o de trabajo y nunca a más de 30 pies por debajo.
Inspecciónelo una vez a la semana.
Los objetos que caigan dentro de las redes de seguridad deben retirarse lo antes posible.
Sistemas de protección contra caídas I
Notes: 1926.502(c)"Safety net systems." Safety net systems and their use shall comply with the following provisions:
1926.502(c)(1)Safety nets shall be installed as close as practicable under the walking/working surface on which employees are working, but in no case more than 30 feet (9.1 m) below such level. When nets are used on bridges, the potential fall area from the walking/working surface to the net shall be unobstructed.
1926.502(c)(2)Safety nets shall extend outward from the outermost projection of the work surface as follows:
____________________________________________________________________ | Vertical distance from working | Minimum required horizontal level to horizontal plane |distance of outer edge of net of net | from the edge of the working | surface _____________________________________|_____________________________ | Up to 5 feet ........................| 8 feet. More than 5 feet up to 10 feet ......| 10 feet. More than 10 feet ...................| 13 feet. _____________________________________|_____________________________
1926.502(c)(3)Safety nets shall be installed with sufficient clearance under them to prevent contact with the surface or structures below when subjected to an impact force equal to the drop test specified in paragraph (c)(4) of this section.
1926.502(c)(4)Safety nets and their installations shall be capable of absorbing an impact force equal to that produced by the drop test specified in paragraph (c)(4)(i) of this section.
1926.502(c)(4)(i)Except as provided in paragraph (c)(4)(ii) of this section, safety nets and safety net installations shall be drop-tested at the jobsite after initial installation and before being used as a fall protection system, whenever relocated, after major repair, and at 6-month intervals if left in one place. The drop-test shall consist of a 400 pound (180 kg) bag of sand 30 + or - 2 inches (76 + or - 5 cm) in diameter dropped into the net from the highest walking/working surface at which employees are exposed to fall hazards, but not from less than 42 inches (1.1 m) above that level.
1926.502(c)(4)(ii)When the employer can demonstrate that it is unreasonable to perform the drop-test required by paragraph (c)(4)(i) of this section, the employer (or a designated competent person) shall certify that the net and net installation is in compliance with the provisions of paragraphs (c)(3) and (c)(4)(i) of this section by preparing a certification record prior to the net being used as a fall protection system. The certification record must include an identification of the net and net installation for which the certification record is being prepared; the date that it was determined that the identified net and net installation were in compliance with paragraph (c)(3) of this section and the signature of the person making the determination and certification. The most recent certification record for each net and net installation shall be available at the jobsite for inspection.
1926.502(c)(5)Defective nets shall not be used. Safety nets shall be inspected at least once a week for wear, damage, and other deterioration. Defective components shall be removed from service. Safety nets shall also be inspected after any occurrence which could affect the integrity of the safety net system.
1926.502(c)(6)Materials, scrap pieces, equipment, and tools which have fallen into the safety net shall be removed as soon as possible from the net and at least before the next work shift.
1926.502(c)(7)The maximum size of each safety net mesh opening shall not exceed 36 square inches (230 cm) nor be longer than 6 inches (15 cm) on any side, and the opening, measured center-to-center of mesh ropes or webbing, shall not be longer than 6 inches (15 cm). All mesh crossings shall be secured to prevent enlargement of the mesh opening.
1926.502(c)(8)Each safety net (or section of it) shall have a border rope for webbing with a minimum breaking strength of 5,000 pounds (22.2 kN).
1926.502(c)(9)Connections between safety net panels shall be as strong as integral net components and shall be spaced not more than 6 inches (15 cm) apart.

## Slide 14: Sistemas de redes de seguridad 2
Sistemas de protección contra caídas I
Notes: 1926.502(c)"Safety net systems." Safety net systems and their use shall comply with the following provisions:
1926.502(c)(1)Safety nets shall be installed as close as practicable under the walking/working surface on which employees are working, but in no case more than 30 feet (9.1 m) below such level. When nets are used on bridges, the potential fall area from the walking/working surface to the net shall be unobstructed.
1926.502(c)(2)Safety nets shall extend outward from the outermost projection of the work surface as follows:
____________________________________________________________________ | Vertical distance from working | Minimum required horizontal level to horizontal plane |distance of outer edge of net of net | from the edge of the working | surface _____________________________________|_____________________________ | Up to 5 feet ........................| 8 feet. More than 5 feet up to 10 feet ......| 10 feet. More than 10 feet ...................| 13 feet. _____________________________________|_____________________________
1926.502(c)(3)Safety nets shall be installed with sufficient clearance under them to prevent contact with the surface or structures below when subjected to an impact force equal to the drop test specified in paragraph (c)(4) of this section.
1926.502(c)(4)Safety nets and their installations shall be capable of absorbing an impact force equal to that produced by the drop test specified in paragraph (c)(4)(i) of this section.
1926.502(c)(4)(i)Except as provided in paragraph (c)(4)(ii) of this section, safety nets and safety net installations shall be drop-tested at the jobsite after initial installation and before being used as a fall protection system, whenever relocated, after major repair, and at 6-month intervals if left in one place. The drop-test shall consist of a 400 pound (180 kg) bag of sand 30 + or - 2 inches (76 + or - 5 cm) in diameter dropped into the net from the highest walking/working surface at which employees are exposed to fall hazards, but not from less than 42 inches (1.1 m) above that level.
1926.502(c)(4)(ii)When the employer can demonstrate that it is unreasonable to perform the drop-test required by paragraph (c)(4)(i) of this section, the employer (or a designated competent person) shall certify that the net and net installation is in compliance with the provisions of paragraphs (c)(3) and (c)(4)(i) of this section by preparing a certification record prior to the net being used as a fall protection system. The certification record must include an identification of the net and net installation for which the certification record is being prepared; the date that it was determined that the identified net and net installation were in compliance with paragraph (c)(3) of this section and the signature of the person making the determination and certification. The most recent certification record for each net and net installation shall be available at the jobsite for inspection.
1926.502(c)(5)Defective nets shall not be used. Safety nets shall be inspected at least once a week for wear, damage, and other deterioration. Defective components shall be removed from service. Safety nets shall also be inspected after any occurrence which could affect the integrity of the safety net system.
1926.502(c)(6)Materials, scrap pieces, equipment, and tools which have fallen into the safety net shall be removed as soon as possible from the net and at least before the next work shift.
1926.502(c)(7)The maximum size of each safety net mesh opening shall not exceed 36 square inches (230 cm) nor be longer than 6 inches (15 cm) on any side, and the opening, measured center-to-center of mesh ropes or webbing, shall not be longer than 6 inches (15 cm). All mesh crossings shall be secured to prevent enlargement of the mesh opening.
1926.502(c)(8)Each safety net (or section of it) shall have a border rope for webbing with a minimum breaking strength of 5,000 pounds (22.2 kN).
1926.502(c)(9)Connections between safety net panels shall be as strong as integral net components and shall be spaced not more than 6 inches (15 cm) apart.

## Slide 15: Sistemas de redes de seguridad 3
Extensión hacia el exterior de las redes de seguridad
Distancia vertical a la red | Distancia horizontal desde el borde de trabajo
Hasta 5 pies | 8 pies
Hasta 10 pies | 10 pies
Más de 10 pies | 13 pies
Sistemas de protección contra caídas I
Notes: 1926.502(c)"Safety net systems." Safety net systems and their use shall comply with the following provisions:
1926.502(c)(1)Safety nets shall be installed as close as practicable under the walking/working surface on which employees are working, but in no case more than 30 feet (9.1 m) below such level. When nets are used on bridges, the potential fall area from the walking/working surface to the net shall be unobstructed.
1926.502(c)(2)Safety nets shall extend outward from the outermost projection of the work surface as follows:
____________________________________________________________________ | Vertical distance from working | Minimum required horizontal level to horizontal plane |distance of outer edge of net of net | from the edge of the working | surface _____________________________________|_____________________________ | Up to 5 feet ........................| 8 feet. More than 5 feet up to 10 feet ......| 10 feet. More than 10 feet ...................| 13 feet. _____________________________________|_____________________________
1926.502(c)(3)Safety nets shall be installed with sufficient clearance under them to prevent contact with the surface or structures below when subjected to an impact force equal to the drop test specified in paragraph (c)(4) of this section.
1926.502(c)(4)Safety nets and their installations shall be capable of absorbing an impact force equal to that produced by the drop test specified in paragraph (c)(4)(i) of this section.
1926.502(c)(4)(i)Except as provided in paragraph (c)(4)(ii) of this section, safety nets and safety net installations shall be drop-tested at the jobsite after initial installation and before being used as a fall protection system, whenever relocated, after major repair, and at 6-month intervals if left in one place. The drop-test shall consist of a 400 pound (180 kg) bag of sand 30 + or - 2 inches (76 + or - 5 cm) in diameter dropped into the net from the highest walking/working surface at which employees are exposed to fall hazards, but not from less than 42 inches (1.1 m) above that level.
1926.502(c)(4)(ii)When the employer can demonstrate that it is unreasonable to perform the drop-test required by paragraph (c)(4)(i) of this section, the employer (or a designated competent person) shall certify that the net and net installation is in compliance with the provisions of paragraphs (c)(3) and (c)(4)(i) of this section by preparing a certification record prior to the net being used as a fall protection system. The certification record must include an identification of the net and net installation for which the certification record is being prepared; the date that it was determined that the identified net and net installation were in compliance with paragraph (c)(3) of this section and the signature of the person making the determination and certification. The most recent certification record for each net and net installation shall be available at the jobsite for inspection.
1926.502(c)(5)Defective nets shall not be used. Safety nets shall be inspected at least once a week for wear, damage, and other deterioration. Defective components shall be removed from service. Safety nets shall also be inspected after any occurrence which could affect the integrity of the safety net system.
1926.502(c)(6)Materials, scrap pieces, equipment, and tools which have fallen into the safety net shall be removed as soon as possible from the net and at least before the next work shift.
1926.502(c)(7)The maximum size of each safety net mesh opening shall not exceed 36 square inches (230 cm) nor be longer than 6 inches (15 cm) on any side, and the opening, measured center-to-center of mesh ropes or webbing, shall not be longer than 6 inches (15 cm). All mesh crossings shall be secured to prevent enlargement of the mesh opening.
1926.502(c)(8)Each safety net (or section of it) shall have a border rope for webbing with a minimum breaking strength of 5,000 pounds (22.2 kN).
1926.502(c)(9)Connections between safety net panels shall be as strong as integral net components and shall be spaced not more than 6 inches (15 cm) apart.

## Slide 16: Sistemas de redes de seguridad 4
Las pruebas de caída son necesarias para garantizar que las redes de seguridad y las instalaciones de redes de seguridad estén funcionando correctamente. Consulte el Título 29 del CFR, parte 1926.502(c)(4)(i) para obtener más información.
    Si un empleador puede demostrar que no es razonable realizar una prueba de caída, el empleador o una persona competente designada deben certificar que la red y su instalación cumplen con la norma.
    Consulte el Título 29 del CFR, parte 1926.502(c)(4)(ii) para obtener más información sobre la certificación y los registros de certificación.
Sistemas de protección contra caídas I
Notes: 1926.502(c)"Safety net systems." Safety net systems and their use shall comply with the following provisions:
1926.502(c)(1)Safety nets shall be installed as close as practicable under the walking/working surface on which employees are working, but in no case more than 30 feet (9.1 m) below such level. When nets are used on bridges, the potential fall area from the walking/working surface to the net shall be unobstructed.
1926.502(c)(2)Safety nets shall extend outward from the outermost projection of the work surface as follows:
____________________________________________________________________ | Vertical distance from working | Minimum required horizontal level to horizontal plane |distance of outer edge of net of net | from the edge of the working | surface _____________________________________|_____________________________ | Up to 5 feet ........................| 8 feet. More than 5 feet up to 10 feet ......| 10 feet. More than 10 feet ...................| 13 feet. _____________________________________|_____________________________
1926.502(c)(3)Safety nets shall be installed with sufficient clearance under them to prevent contact with the surface or structures below when subjected to an impact force equal to the drop test specified in paragraph (c)(4) of this section.
1926.502(c)(4)Safety nets and their installations shall be capable of absorbing an impact force equal to that produced by the drop test specified in paragraph (c)(4)(i) of this section.
1926.502(c)(4)(i)Except as provided in paragraph (c)(4)(ii) of this section, safety nets and safety net installations shall be drop-tested at the jobsite after initial installation and before being used as a fall protection system, whenever relocated, after major repair, and at 6-month intervals if left in one place. The drop-test shall consist of a 400 pound (180 kg) bag of sand 30 + or - 2 inches (76 + or - 5 cm) in diameter dropped into the net from the highest walking/working surface at which employees are exposed to fall hazards, but not from less than 42 inches (1.1 m) above that level.
1926.502(c)(4)(ii)When the employer can demonstrate that it is unreasonable to perform the drop-test required by paragraph (c)(4)(i) of this section, the employer (or a designated competent person) shall certify that the net and net installation is in compliance with the provisions of paragraphs (c)(3) and (c)(4)(i) of this section by preparing a certification record prior to the net being used as a fall protection system. The certification record must include an identification of the net and net installation for which the certification record is being prepared; the date that it was determined that the identified net and net installation were in compliance with paragraph (c)(3) of this section and the signature of the person making the determination and certification. The most recent certification record for each net and net installation shall be available at the jobsite for inspection.
1926.502(c)(5)Defective nets shall not be used. Safety nets shall be inspected at least once a week for wear, damage, and other deterioration. Defective components shall be removed from service. Safety nets shall also be inspected after any occurrence which could affect the integrity of the safety net system.
1926.502(c)(6)Materials, scrap pieces, equipment, and tools which have fallen into the safety net shall be removed as soon as possible from the net and at least before the next work shift.
1926.502(c)(7)The maximum size of each safety net mesh opening shall not exceed 36 square inches (230 cm) nor be longer than 6 inches (15 cm) on any side, and the opening, measured center-to-center of mesh ropes or webbing, shall not be longer than 6 inches (15 cm). All mesh crossings shall be secured to prevent enlargement of the mesh opening.
1926.502(c)(8)Each safety net (or section of it) shall have a border rope for webbing with a minimum breaking strength of 5,000 pounds (22.2 kN).
1926.502(c)(9)Connections between safety net panels shall be as strong as integral net components and shall be spaced not more than 6 inches (15 cm) apart.

## Slide 17: Sistemas de redes de seguridad 5
Para funcionar correctamente, una red de seguridad debe tener aberturas seguras. Las aberturas de la malla no deben superar las 36 pulgadas cuadradas y no deben ser más largas de 6 pulgadas en cualquier lado. Cada abertura, medida de centro a centro de las cuerdas de la malla o red, no debe superar las 6 pulgadas. Título 29 del CFR, parte 1926.502(c)(7).
Todos los cruces de la malla deben estar asegurados para evitar que las aberturas se agranden. Título 29 del CFR, parte 1926.502(c)(7).
Utilice una red de seguridad (o una parte de la red) con una cuerda de borde que posea una resistencia mínima a la rotura de 5,000 libras. Título 29 del CFR, parte 1926.502(c)(8).
No permita que un tramo débil comprometa una red de seguridad. Utilice conexiones entre los paneles de la red de seguridad que sean tan resistentes como los componentes integrales de la red y que no estén separados más de 6 pulgadas. Título 29 del CFR, parte 1926.502(c)(9).
Sistemas de protección contra caídas I
Notes: 1926.502(c)"Safety net systems." Safety net systems and their use shall comply with the following provisions:
1926.502(c)(1)Safety nets shall be installed as close as practicable under the walking/working surface on which employees are working, but in no case more than 30 feet (9.1 m) below such level. When nets are used on bridges, the potential fall area from the walking/working surface to the net shall be unobstructed.
1926.502(c)(2)Safety nets shall extend outward from the outermost projection of the work surface as follows:
____________________________________________________________________ | Vertical distance from working | Minimum required horizontal level to horizontal plane |distance of outer edge of net of net | from the edge of the working | surface _____________________________________|_____________________________ | Up to 5 feet ........................| 8 feet. More than 5 feet up to 10 feet ......| 10 feet. More than 10 feet ...................| 13 feet. _____________________________________|_____________________________
1926.502(c)(3)Safety nets shall be installed with sufficient clearance under them to prevent contact with the surface or structures below when subjected to an impact force equal to the drop test specified in paragraph (c)(4) of this section.
1926.502(c)(4)Safety nets and their installations shall be capable of absorbing an impact force equal to that produced by the drop test specified in paragraph (c)(4)(i) of this section.
1926.502(c)(4)(i)Except as provided in paragraph (c)(4)(ii) of this section, safety nets and safety net installations shall be drop-tested at the jobsite after initial installation and before being used as a fall protection system, whenever relocated, after major repair, and at 6-month intervals if left in one place. The drop-test shall consist of a 400 pound (180 kg) bag of sand 30 + or - 2 inches (76 + or - 5 cm) in diameter dropped into the net from the highest walking/working surface at which employees are exposed to fall hazards, but not from less than 42 inches (1.1 m) above that level.
1926.502(c)(4)(ii)When the employer can demonstrate that it is unreasonable to perform the drop-test required by paragraph (c)(4)(i) of this section, the employer (or a designated competent person) shall certify that the net and net installation is in compliance with the provisions of paragraphs (c)(3) and (c)(4)(i) of this section by preparing a certification record prior to the net being used as a fall protection system. The certification record must include an identification of the net and net installation for which the certification record is being prepared; the date that it was determined that the identified net and net installation were in compliance with paragraph (c)(3) of this section and the signature of the person making the determination and certification. The most recent certification record for each net and net installation shall be available at the jobsite for inspection.
1926.502(c)(5)Defective nets shall not be used. Safety nets shall be inspected at least once a week for wear, damage, and other deterioration. Defective components shall be removed from service. Safety nets shall also be inspected after any occurrence which could affect the integrity of the safety net system.
1926.502(c)(6)Materials, scrap pieces, equipment, and tools which have fallen into the safety net shall be removed as soon as possible from the net and at least before the next work shift.
1926.502(c)(7)The maximum size of each safety net mesh opening shall not exceed 36 square inches (230 cm) nor be longer than 6 inches (15 cm) on any side, and the opening, measured center-to-center of mesh ropes or webbing, shall not be longer than 6 inches (15 cm). All mesh crossings shall be secured to prevent enlargement of the mesh opening.
1926.502(c)(8)Each safety net (or section of it) shall have a border rope for webbing with a minimum breaking strength of 5,000 pounds (22.2 kN).
1926.502(c)(9)Connections between safety net panels shall be as strong as integral net components and shall be spaced not more than 6 inches (15 cm) apart.

## Slide 18: Factores de diseño del sistema de detención de caídas
El objetivo de un sistema de detención de caídas es reducir el riesgo de lesiones provocadas por una caída accidental a un nivel aceptable.
El riesgo de lesiones por una caída nunca puede eliminarse, solo reducirse.
La distancia a la que cae un trabajador antes de que el equipo de amortiguación o desaceleración empiece a surtir efecto
    afecta tanto a las fuerzas de impacto como a la distancia total de caída.
Sistemas de protección contra caídas I

## Slide 19: Principales inquietudes 1
Fuerza de impacto en el cuerpo inferior a 1800 (con un arnés).
Distancia máxima de caída libre de 6 pies.
No puede golpear estructuras inferiores.
Peso máximo de la persona con herramientas según la clasificación del fabricante.
Cuando se utiliza un sistema detención de caídas, debe estar diseñado para utilizarse todo el tiempo.
Sistemas de protección contra caídas I

## Slide 20: Principales inquietudes 2
¿Hasta dónde caeré antes de que me detenga por completo?
¿Con qué me golpearé en la caída?
¿Cómo me bajarán?
Sistemas de protección contra caídas I

## Slide 21: Sistemas personales de detención de caídas (PFAS)
Dispositivos de conexión (cuerda de seguridad amortiguadora con mosquetones de bloqueo)
Vestimenta corporal (arnés de cuerpo completo)
Punto de anclaje/punto de amarre
Sistemas de protección contra caídas I

## Slide 22: Punto de anclaje 1
Los elementos de sujeción utilizados para la fijación del equipo personal de detención de caídas serán independientes de cualquier anclaje que se utilice para soportar o suspender plataformas.
Ser capaces de soportar al menos 5,000 libras por cada empleado amarrado.
    3000 libras cuando se utiliza un sistema de retención de caídas o una cuerda salvavidas autorretráctil (SRL, retráctil o “yoyó”) que limita la distancia de caída libre de 2 a 4.5 pies.
Se diseñarán, instalarán y utilizarán como se indica a continuación:
    Como parte de un sistema personal de detención de caídas completo que mantenga un factor de seguridad de al menos dos.
    Bajo la supervisión de una persona calificada.
Sistemas de protección contra caídas I
Notes: NOTE---HORIZONTAL LIFELINES---ONLY OPTION IS TWICE MAXIMUM ARRESTING FORCE – which will require some calculation, unless using a manufactured system in accordance with the manufacturers’ requirements
1926.502(d)(8)Horizontal lifelines shall be designed, installed, and used, under the supervision of a qualified person, as part of a complete personal fall arrest system, which maintains a safety factor of at least two.

## Slide 23: Punto de anclaje 2
Debe limitar la distancia de caída a 6 pies antes de la desaceleración y los arneses no deben ejercer más de 1,800 libras de fuerza de impacto sobre el cuerpo.
ANSI exige no más de 900 libras de fuerza sobre el cuerpo.
Sistemas de protección contra caídas I
Notes: 1926.502(d)(15)Anchorages used for attachment of personal fall arrest equipment shall be independent of any anchorage being used to support or suspend platforms and capable of supporting at least 5,000 pounds (22.2 kN) per employee attached, or shall be designed, installed, and used as follows:
1926.502(d)(9)Lanyards and vertical lifelines shall have a minimum breaking strength of 5,000 pounds (22.2 kN).

## Slide 24: Tipos de anclajes 1
Anclaje superior (uno o dos anillos en D)
Anclaje de cercha (incluso el separador)
Abrazadera para vigas I y acero estructural (vigas verticales u horizontales)
Anclaje de monoviga
Anclaje para techado de chapa
Eslinga de anclaje de cables
Anclaje de correa (red)
Sistemas de protección contra caídas I

## Slide 25: Tipos de anclajes 2
Anclajes de hormigón
Anclaje de pared atornillado
Mástil de anclaje retráctil giratorio
Sistema de protección contra caídas móvil
Anclaje de peso muerto
Sistemas de protección contra caídas I

## Slide 26: Tipos de anclajes 3
Abrazadera de viga de madera
Anclaje de abrazadera de tubería
Anclajes atornillados
Cuerdas de seguridad de amarre envolventes
Sistemas de protección contra caídas I

## Slide 27: Punto de anclaje 3
¿Qué sucede si no tengo un punto de anclaje identificado?
    Utilice una viga estructural de la construcción.
    ¿Qué sucede si no sé qué fuerza soportará mi punto de anclaje?
    Minimice la fuerza de detención.
Los ingenieros necesitan tiempo para hacer su trabajo: ¡la planificación previa es clave!
Sistemas de protección contra caídas I

## Slide 28: Dispositivos de conexión (cuerdas de seguridad) 1
Cuerdas de seguridad de una sola pierna
El tipo más común de absorbedor de impacto es una funda de punto de desgarro que se fija integralmente a una cuerda de seguridad para la detención de la caída o a una cuerda de seguridad cosida.
Cuerdas de seguridad de dos piernas
Se recomienda como opción para mantener el 100% de la protección contra caídas en movimiento, donde una cuerda de seguridad está enganchada en todo momento.
Sistemas de protección contra caídas I

## Slide 29: Dispositivos de conexión (cuerdas de seguridad) 2
Cuerdas salvavidas retráctiles - Cuerdas salvavidas autorretráctiles (SRL)
Muy eficaces para aplicaciones verticales.
Normalmente se bloquean en 2 a 4.5 pies. Así, minimizan la distancia total de caída y las fuerzas de impacto en el cuerpo del trabajador.
Sistemas de protección contra caídas I
Notes: 1926.502(d)(16)(v)have sufficient strength to withstand twice the potential impact energy of an employee free falling a distance of 6 feet (1.8 m), or the free fall distance permitted by the system, whichever is less. Note: If the personal fall arrest system meets the criteria and protocols contained in Appendix C to subpart M, and if the system is being used by an employee having a combined person and tool weight of less than 310 pounds (140 kg), the system will be considered to be in compliance with the provisions of paragraph (d)(16) of this section. If the system is used by an employee having a combined tool and body weight of 310 pounds (140 kg) or more, then the employer must appropriately modify the criteria and protocols of the Appendix to provide proper protection for such heavier weights, or the system will not be deemed to be in compliance with the requirements of paragraph (d)(16) of this section.

## Slide 30: Dispositivos de conexión (cuerdas de seguridad) 3
Los trabajadores que se alejan de los dispositivos retráctiles están expuestos a caídas pendulares.
Los elementos retráctiles deberán fijarse directamente al arnés o a un extensor de anillo en D.
Las cuerdas salvavidas autorretráctiles y las cuerdas de seguridad que limitan automáticamente la distancia de caída libre a 2 pies o menos deben ser capaces de soportar una carga de tracción mínima de 3,000 libras aplicada al dispositivo con la cuerda salvavidas o la cuerda de seguridad en posición totalmente extendida.
Indicador de caída
Desplegado
Sistemas de protección contra caídas I
Notes: 1926.502(d)(12)Self-retracting lifelines and lanyards which automatically limit free fall distance to 2 feet (0.61 m) or less shall be capable of sustaining a minimum tensile load of 3,000 pounds (13.3 kN) applied to the device with the lifeline or lanyard in the fully extended position.
1926.502(d)(15)Anchorages used for attachment of personal fall arrest equipment shall be independent of any anchorage being used to support or suspend platforms and capable of supporting at least 5,000 pounds (22.2 kN) per employee attached, or shall be designed, installed, and used as follows:
1926.502(d)(15)(i)as part of a complete personal fall arrest system which maintains a safety factor of at least two; and
1926.502(d)(15)(ii)under the supervision of a qualified person.

## Slide 31: Sogas de seguridad 1
El gancho de la soga de detención de caídas se desplaza por una cuerda salvavidas y se engancha automáticamente a esta para detener la caída accidental de una persona.
Se utiliza en sistemas verticales y horizontales.
La cuerda de seguridad utilizada con el gancho de la soga de detención de caídas y la cuerda salvavidas vertical no deben tener más de tres (3) pies de longitud y deben contener un dispositivo absorbedor de energía.
Sistemas de protección contra caídas I

## Slide 32: Sogas de seguridad 2
Sistemas de protección contra caídas I

## Slide 33: Cuerdas salvavidas horizontales 1
Las cuerdas salvavidas horizontales requieren una atención especial durante el diseño y la instalación para cumplir con lo siguiente:
    Limitar la distancia a la que puede caer el trabajador (una mayor inclinación en la cuerda puede significar una caída más lejana).
    Minimizar las fuerzas en los conectores en el anclaje (una mayor inclinación en la cuerda puede significar menores fuerzas sobre los conectores del anclaje en cualquiera de los extremos).
    Una persona calificada debe supervisar el diseño, la instalación y el uso de la cuerda salvavidas horizontal.
Temporal
Permanente
Sistemas de protección contra caídas I
Notes: 502(d)(8) Shall be designed, installed, and used, under the supervision of a qualified person, as part of a complete personal fall arrest system, which maintains a safety factor of at least two.

## Slide 34: Cuerdas salvavidas horizontales 2
Servir como cuerdas de anclaje que se colocan entre puntos de anclaje fijos en el mismo nivel.
Cuerdas salvavidas horizontales (Horizontal Lifelines, HLL) diseñadas para ayudar a minimizar el riesgo de la caída "pendular".
Deben colocarse a una altura por encima de la cintura.
Sistemas de protección contra caídas I

## Slide 35: Cuerdas salvavidas horizontales 3
Dependiendo de su geometría y ángulo de inclinación, las cuerdas salvavidas horizontales pueden estar sometidas a cargas mayores que la carga de impacto impuesta por un componente unido.
Cuando la inclinación de la cuerda salvavidas horizontal es inferior a 30 grados, la fuerza de impacto ejercida a la cuerda salvavidas por una cuerda de seguridad unida se amplifica notablemente.
    Una inclinación de 150 amplifica la fuerza aproximadamente 2:1.
    Una inclinación de 50 amplifica la fuerza aproximadamente 6:1.
Sistemas de protección contra caídas I

## Slide 36: Cuerdas salvavidas horizontales 4
¿Cuáles son los peligros?
Caída pendular.
Efecto “péndulo”.
Si no están bien diseñadas, podría chocar contra el suelo.
Sistemas de protección contra caídas I

## Slide 37: Cuerpo (arneses) 1
El arnés debe ser del tamaño adecuado para el trabajador.
Se lo debe inspeccionar frecuentemente (a diario antes de su uso por el trabajador, al menos una vez al mes por una persona competente).
Nunca debe modificarse.
Debe retirarse de servicio inmediatamente si está defectuoso o fue expuesto a un impacto.
Correa pectoral ajustada a la mitad del pecho
Correas de las piernas ajustadas, pero sin apretar
La correa subpélvica (“trasera”) soporta la carga.
Anillo en “D” entre los omóplatos
Sistemas de protección contra caídas I

## Slide 38: Cuerpo (arneses) 2
Reglas de oro
    Poder alcanzar su anillo en D con el pulgar
    Máximo cuatro dedos (planos) de holgura en las piernas, correas tan altas como sea cómodamente posible
    Asegurarse de que la correa del pecho pase por el pecho o el esternón
    Haga que un compañero compruebe que las correas no estén giradas, etc.
Sistemas de protección contra caídas I

## Slide 39: Sistemas personales de detención de caídas (PFAS) 1
El objetivo de un sistema de detención de caídas es reducir el riesgo de lesiones provocadas por una caída accidental a un nivel aceptable.
    El riesgo de lesiones por una caída nunca puede eliminarse, solo reducirse.
La distancia a la que cae un trabajador antes de que el equipo de amortiguación o desaceleración empiece a surtir efecto afecta tanto a las fuerzas de impacto como a la distancia total de caída.
Ubicación del punto de anclaje en relación con la altura del anillo en D:
    Por debajo del anillo en D permite caídas excesivas.
    Por encima del anillo en D minimiza la caída libre a menos de 6 pies.
Sistemas de protección contra caídas I

## Slide 40: Anclaje al nivel del pie
Cuerda de seguridad de 6 pies
3 ½ pies de distancia de desaceleración
6 pies desde el elemento de sujeción hasta el pie
Factor de seguridad de 3 pies
23 ½ pies en total
18 ½ pies del nivel inferior
5 pies antes de que el anillo en D pase por el punto de anclaje
Total de 11 pies de distancia de desplazamiento del anillo en D antes de que la detención de la caída surta efecto. Esta fuerza de impacto potencial supera la capacidad de muchas cuerdas de seguridad (y las normas de la OSHA).
Todas las distancias son aproximadas y se muestran solo a título ilustrativo. Por lo tanto, es fundamental mantener la distancia del factor de seguridad.
Sistemas de protección contra caídas I

## Slide 41: Anclaje al nivel del hombro
Sistemas de protección contra caídas I

## Slide 42: Anclaje en altura
Sistemas de protección contra caídas I

## Slide 43: Sistemas personales de detención de caídas (PFAS) 2
Aunque utilice un sistema de detención de caídas, su cuerpo no se frenará a un ritmo uniforme: algunas partes experimentarán una aceleración localizada en relación con otras.
La duración y la distancia de su desaceleración, así como el grado de tensión que sufren algunas partes del cuerpo, dependen de muchos factores, entre ellos, los siguientes:
    peso
    distancia de caída
    características del sistema detención de caídas
    orientación del cuerpo al inicio de la desaceleración
Sistemas de protección contra caídas I

## Slide 44: Ejercicio de distancia de caída
Estos trabajadores están atados a las vigas en las que están parados con eslingas corredizas.
¿A qué distancia caerán?
Calcule la distancia de caída libre.
Calcule la distancia de caída total.
Sistemas de protección contra caídas I

## Slide 45: Sistemas personales de detención de caídas (PFAS) 3
Caída pendular
A
B
Obstrucciones
Sistemas de protección contra caídas I

## Slide 46: Rescate de caídas 1
La fase de suspensión de una caída dura hasta que lo rescatan (suponiendo que no pueda recuperar el equilibrio sin ayuda).
Puede estar inconsciente o incapacitado de algún modo.
Su tolerancia a la suspensión sin riesgo de lesiones graves o muerte es relativamente corta, en especial si no está en condiciones físicas óptimas. (15 a 20) minutos
    Aparecerá la intolerancia ortostática.
Distribuya la carga entre la correa del muslo y la correa del cinturón si se usa un arnés.
El exceso de presión aquí puede cortar el flujo sanguíneo a las piernas.
Sistemas de protección contra caídas I
Notes: 1926.502(d)(20)
The employer shall provide for prompt rescue of employees in the event of a fall or shall assure that employees are able to rescue themselves.

## Slide 47: Rescate de caídas Factores que pueden afectar el grado de riesgo de traumatismo por suspensión:2
Incapacidad de mover las piernas | Hipotermia
Dolor | Impacto
Lesiones durante la caída | Enfermedad cardiovascular
Fatiga | Enfermedad respiratoria
Deshidratación | Pérdida de sangre
Referencias: Seddon, Paul. Harness Suspension: review and evaluation of existing information (Suspensión en arnés: revisión y evaluación de la información existente). Ejecutivo de Seguridad y Salud. Informe de investigación 451/2002. 104 páginas.
El empleador deberá prever el rescate inmediato de los trabajadores en caso de una caída o asegurase de que los trabajadores sean capaces de rescatarse a sí mismos. Debe existir un plan para recuperar o rescatar a un trabajador que haya sufrido una caída.
Sistemas de protección contra caídas I
Notes: 1926.502(d)(20)
The employer shall provide for prompt rescue of employees in the event of a fall or shall assure that employees are able to rescue themselves.

## Slide 48: Rescate de caídas 3
Rescate
    Autorrescate: primario
      Con el equipo de protección personal contra caídas adecuado, la capacitación y la práctica, un trabajador que haya sufrido una caída puede tomar medidas para minimizar el traumatismo por suspensión. Los métodos de autorrescate permiten a un trabajador que haya sufrido una caída aliviar temporalmente la presión en las piernas o, en algunos casos, incluso descender él mismo al nivel inferior.
Sistemas de protección contra caídas I
Notes: 1926.502(d)(20)
The employer shall provide for prompt rescue of employees in the event of a fall or shall assure that employees are able to rescue themselves.

## Slide 49: Rescate de caídas 4
Rescate
    Rescate asistido: secundario
      Un trabajador que está suspendido de una cuerda salvavidas y no puede realizar un autorrescate necesitará ayuda del personal de rescate capacitado que utilice el equipo correcto, incluida la protección contra caídas adecuada.
Sistemas de protección contra caídas I
Notes: 1926.502(d)(20)
The employer shall provide for prompt rescue of employees in the event of a fall or shall assure that employees are able to rescue themselves.

## Slide 50: Rescate de caídas 5
Rescate
    Rescate profesional: última opción
      El personal de respuesta a emergencias fuera del sitio puede rescatar a los trabajadores suspendidos, aunque la mayoría de los socorristas del 911 no está capacitada para hacerlo.
      ¿Tiempo de respuesta?
Sistemas de protección contra caídas I
Notes: 1926.502(d)(20)
The employer shall provide for prompt rescue of employees in the event of a fall or shall assure that employees are able to rescue themselves.

## Slide 51: Rescate de caídas 6
Cuando funciona
Sistemas de protección contra caídas I
Notes: 1926.502(d)(20)
The employer shall provide for prompt rescue of employees in the event of a fall or shall assure that employees are able to rescue themselves.

## Slide 52: ¿Tiene preguntas?
Sistemas de protección contra caídas I