## Slide 1: Andamios, escaleras móviles y jirafas
Prevención de caídas en la construcción

## Slide 2: Objetivos de aprendizaje
Comprensión de los requisitos generales para el uso seguro de andamios
Comprensión de cómo mantener una posición segura al utilizar escaleras móviles
Comprensión de cómo colocar correctamente las escaleras móviles
Identificación de los requisitos de protección contra caídas de la OSHA durante el uso de jirafas
Andamios, escaleras móviles y jirafas

## Slide 3: Un poco de planificación podría haber evitado esto.
Andamios, escaleras móviles y jirafas

## Slide 4: Acceso
No hay acceso por los refuerzos transversales.
El peldaño inferior no puede estar a más de 24 pulgadas por encima del nivel inferior.
Debe utilizar una escalera móvil o armazones diseñados para ser utilizados como escaleras.
Andamios, escaleras móviles y jirafas
Notes: "Access." This paragraph applies to scaffold access for all employees. Access requirements for employees erecting or dismantling supported scaffolds are specifically addressed in paragraph (e)(9) of this section.
1926.451(e)(1) When scaffold platforms are more than 2 feet (0.6 m) above or below a point of access, portable ladders, hook-on ladders, attachable ladders, stair towers (scaffold stairways/towers), stairway-type ladders (such as ladder stands), ramps, walkways, integral prefabricated scaffold access, or direct access from another scaffold, structure, personnel hoist, or similar surface shall be used. Crossbraces shall not be used as a means of access.
1926.451(e)(2) Portable, hook-on, and attachable ladders (Additional requirements for the proper construction and use of portable ladders are contained in subpart X of this part -- Stairways and Ladders):

## Slide 5: Acceso correcto
Plataforma de escalera móvil
Armazón de la escalera fija
Armazón de la escalera móvil
Escalera móvil atada al andamio
Andamios, escaleras móviles y jirafas
Notes: Ladder frame must be uniform and less than 16-3/4 inches.
You should check with the manufacturer’s requirements.

## Slide 6: Barandas para andamios
Se requieren barandas en un andamio de más de 10 pies por encima del nivel inferior.
La práctica recomendada sugiere colocarla en la parte superior del primer nivel.
Debe tener un larguero intermedio.
Andamios, escaleras móviles y jirafas
Notes: 1926.451(g)
"Fall protection.”
1926.451(g)(1)
Each employee on a scaffold more than 10 feet (3.1 m) above a lower level shall be protected from falling to that lower level. Paragraphs (g)(1)(i) through (vii) of this section establish the types of fall protection to be provided to the employees on each type of scaffold. Paragraph (g)(2) of this section addresses fall protection for scaffold erectors and dismantlers.
Note to paragraph (g)(1): The fall protection requirements for employees installing suspension scaffold support systems on floors, roofs, and other elevated surfaces are set forth in subpart M of this part.

## Slide 7: Refuerzos como barandas
Las barandas son las adecuadas mediante el uso de un 2x4 como una baranda y el refuerzo como la otra baranda. Solo si el punto de cruce está entre 38 y 48 pulgadas de altura.
Andamios, escaleras móviles y jirafas
Notes: 1926.451(g)(4)(xv)
Crossbracing is acceptable in place of a midrail when the crossing point of two braces is between 20 inches (0.5 m) and 30 inches (0.8 m) above the work platform or as a toprail when the crossing point of two braces is between 38 inches (0.97 m) and 48 inches (1.3 m) above the work platform. The end points at each upright shall be no more than 48 inches (1.3 m) apart.

## Slide 8: Andamios Baker
Los andamios Baker pueden ser inestables.
Nunca utilice una pila doble sin estabilizadores.
Todas las ruedas deben bloquearse cada vez que se detenga el andamio.
Andamios, escaleras móviles y jirafas
Notes: A minimum of three wheels must be locked when employees are working on the platform, it is recommended that all wheels should be locked when working on the platform.
Where possible, consider the use of scissor lifts when a mobile scaffold is required.

## Slide 9: Andamios suspendidos
Los estabilizadores deben estar correctamente colocados y tener cuerdas de anclaje de seguridad.
Los trabajadores deben tener cuerdas salvavidas independientes.
Se debe proporcionar protección interior si el andamio está a más de 14 pulgadas de la estructura de la pared.
Sin cuerda de anclaje
Andamios, escaleras móviles y jirafas
Notes: 9
Scaffold outriggers that are not secured to the working surface must have appropriate tie-backs in line with the outrigger to a proper anchor separate from the fall arrest anchors.

## Slide 10: Usos inadecuados de escaleras móviles
Andamios, escaleras móviles y jirafas
Notes: 1926.1053(a)General. The following requirements apply to all ladders as indicated, including job-made ladders.
1926.1053(a)(1)Ladders shall be capable of supporting the following loads without failure:
1926.1053(a)(1)(i)Each self-supporting portable ladder: At least four times the maximum intended load, except that each extra-heavy-duty type 1A metal or plastic ladder shall sustain at least 3.3 times the maximum intended load. The ability of a ladder to sustain the loads indicated in this paragraph shall be determined by applying or transmitting the requisite load to the ladder in a downward vertical direction. Ladders built and tested in conformance with the applicable provisions of appendix A of this subpart will be deemed to meet this requirement.
1926.1053(a)(1)(ii)Each portable ladder that is not self-supporting: At least four times the maximum intended load, except that each extra-heavy-duty type 1A metal or plastic ladders shall sustain at least 3.3 times the maximum intended load. The ability of a ladder to sustain the loads indicated in this paragraph shall be determined by applying or transmitting the requisite load to the ladder in a downward vertical direction when the ladder is placed at an angle of 75 1/2 degrees from the horizontal. Ladders built and tested in conformance with the applicable provisions of appendix A will be deemed to meet this requirement.
1926.1053(a)(1)(iii)Each fixed ladder: At least two loads of 250 pounds (114 kg) each, concentrated between any two consecutive attachments (the number and position of additional concentrated loads of 250 pounds (114 kg) each, determined from anticipated usage of the ladder, shall also be included), plus anticipated loads caused by ice buildup, winds, rigging, and impact loads resulting from the use of ladder safety devices. Each step or rung shall be capable of supporting a single concentrated load of at least 250 pounds (114 kg) applied in the middle of the step or rung. Ladders built in conformance with the applicable provisions of appendix A will be deemed to meet this requirement.
1926.1053(a)(2)Ladder rungs, cleats, and steps shall be parallel, level, and uniformly spaced when the ladder is in position for use.
1926.1053(a)(3)(i)Rungs, cleats, and steps of portable ladders (except as provided below) and fixed ladders (including individual-rung/step ladders) shall be spaced not less than 10 inches (25 cm) apart, nor more than 14 inches (36 cm) apart, as measured between center lines of the rungs, cleats, and steps.
1926.1053(a)(3)(ii)Rungs, cleats, and steps of step stools shall be not less than 8 inches (20 cm) apart, nor more than 12 inches (31 cm) apart, as measured between center lines of the rungs, cleats, and steps.
1926.1053(a)(3)(iii)Rungs, cleats, and steps of the base section of extension trestle ladders shall not be less than 8 inches (20 cm) nor more than 18 inches (46 cm) apart, as measured between center lines of the rungs, cleats, and steps. The rung spacing on the extension section of the extension trestle ladder shall be not less than 6 inches (15 cm) nor more than 12 inches (31 cm), as measured between center lines of the rungs, cleats, and steps.
1926.1053(a)(4)(i)The minimum clear distance between the sides of individual-rung/step ladders and the minimum clear distance between the side rails of other fixed ladders shall be 16 inches (41 cm).
1926.1053(a)(4)(ii)The minimum clear distance between side rails for all portable ladders shall be 11 1/2 inches (29 cm).
1926.1053(a)(5)The rungs of individual-rung/step ladders shall be shaped such that employees' feet cannot slide off the end of the rungs.
1926.1053(a)(6)(i)The rungs and steps of fixed metal ladders manufactured after March 15, 1991, shall be corrugated, knurled, dimpled, coated with skid-resistant material, or otherwise treated to minimize slipping.
1926.1053(a)(6)(ii)The rungs and steps of portable metal ladders shall be corrugated, knurled, dimpled, coated with skid-resistant material, or otherwise treated to minimize slipping.
1926.1053(a)(7)Ladders shall not be tied or fastened together to provide longer sections unless they are specifically designed for such use.
1926.1053(a)(8)A metal spreader or locking device shall be provided on each stepladder to hold the front and back sections in an open position when the ladder is being used.
1926.1053(a)(9)When splicing is required to obtain a given length of side rail, the resulting side rail must be at least equivalent in strength to a one-piece side rail made of the same material.
1926.1053(a)(10)Except when portable ladders are used to gain access to fixed ladders (such as those on utility towers, billboards, and other structures where the bottom of the fixed ladder is elevated to limit access), when two or more separate ladders are used to reach an elevated work area, the ladders shall be offset with a platform or landing between the ladders. (The requirements to have guardrail systems with toeboards for falling object and overhead protection on platforms and landings are set forth in subpart M of this part.)
1926.1053(a)(11)Ladder components shall be surfaced so as to prevent injury to an employee from punctures or lacerations, and to prevent snagging of clothing.
1926.1053(a)(12)Wood ladders shall not be coated with any opaque covering, except for identification or warning labels which may be placed on one face only of a side rail.
1926.1053(a)(13)The minimum perpendicular clearance between fixed ladder rungs, cleats, and steps, and any obstruction behind the ladder shall be 7 inches (18 cm), except in the case of an elevator pit ladder, for which a minimum perpendicular clearance of 4 1/2 inches (11 cm) is required.
1926.1053(a)(14)The minimum perpendicular clearance between the center line of fixed ladder rungs, cleats, and steps, and any obstruction on the climbing side of the ladder shall be 30 inches (76 cm), except as provided in paragraph (a)(15) of this section.
1926.1053(a)(15)When unavoidable obstructions are encountered, the minimum perpendicular clearance between the centerline of fixed ladder rungs, cleats, and steps, and the obstruction on the climbing side of the ladder may be reduced to 24 inches (61 cm), provided that a deflection device is installed to guide employees around the obstruction.
1926.1053(a)(16)Through fixed ladders at their point of access/egress shall have a step-across distance of not less than 7 inches (18 cm) nor more than 12 inches (30 cm) as measured from the centerline of the steps or rungs to the nearest edge of the landing area. If the normal step-across distance exceeds 12 inches (30 cm), a landing platform shall be provided to reduce the distance to the specified limit.
1926.1053(a)(17)Fixed ladders without cages or wells shall have a clear width to the nearest permanent object of at least 15 inches (38 cm) on each side of the centerline of the ladder.
1926.1053(a)(18)Fixed ladders shall be provided with cages, wells, ladder safety devices, or self-retracting lifelines where the length of climb is less than 24 feet (7.3 m) but the top of the ladder is at a distance greater than 24 feet (7.3 m) above lower levels.
1926.1053(a)(19)Where the total length of a climb equals or exceeds 24 feet (7.3 m), fixed ladders shall be equipped with one of the following:
1926.1053(a)(19)(i)Ladder safety devices; or
1926.1053(a)(19)(ii)Self-retracting lifelines, and rest platforms at intervals not to exceed 150 feet (45.7 m); or
1926.1053(a)(19)(iii)A cage or well, and multiple ladder sections, each ladder section not to exceed 50 feet (15.2 m) in length. Ladder sections shall be offset from adjacent sections, and landing platforms shall be provided at maximum intervals of 50 feet (15.2 m).
1926.1053(a)(20)Cages for fixed ladders shall conform to all of the following:
1926.1053(a)(20)(i)Horizontal bands shall be fastened to the side rails of rail ladders, or directly to the structure, building, or equipment for individual-rung ladders;
1926.1053(a)(20)(ii)Vertical bars shall be on the inside of the horizontal bands and shall be fastened to them;
1926.1053(a)(20)(iii)Cages shall extend not less than 27 inches (68 cm), or more than 30 inches (76 cm) from the centerline of the step or rung (excluding the flare at the bottom of the cage), and shall not be less than 27 inches (68 cm) in width;
1926.1053(a)(20)(iv)The inside of the cage shall be clear of projections;
1926.1053(a)(20)(v)Horizontal bands shall be spaced not more than 4 feet (1.2 m) on center vertically;
1926.1053(a)(20)(vi)Vertical bars shall be spaced at intervals not more than 9 1/2 inches (24 cm) on center horizontally;
1926.1053(a)(20)(vii)The bottom of the cage shall be at a level not less than 7 feet (2.1 m) nor more than 8 feet (2.4 m) above the point of access to the bottom of the ladder. The bottom of the cage shall be flared not less than 4 inches (10 cm) all around within the distance between the bottom horizontal band and the next higher band;
1926.1053(a)(20)(viii)The top of the cage shall be a minimum of 42 inches (1.1 m) above the top of the platform, or the point of access at the top of the ladder, with provision for access to the platform or other point of access.
1926.1053(a)(21)Wells for fixed ladders shall conform to all of the following:
1926.1053(a)(21)(i)They shall completely encircle the ladder;
1926.1053(a)(21)(ii)They shall be free of projections;
1926.1053(a)(21)(iii)Their inside face on the climbing side of the ladder shall extend not less than 27 inches (68 cm) nor more than 30 inches (76 cm) from the centerline of the step or rung;
1926.1053(a)(21)(iv)The inside clear width shall be at least 30 inches (76 cm);
1926.1053(a)(21)(v)The bottom of the wall on the access side shall start at a level not less than 7 feet (2.1 m) nor more than 8 feet (2.4 m) above the point of access to the bottom of the ladder.
1926.1053(a)(22)Ladder safety devices, and related support systems, for fixed ladders shall conform to all of the following:
1926.1053(a)(22)(i)They shall be capable of withstanding without failure a drop test consisting of an 18-inch (41 cm) drop of a 500-pound (226 kg) weight;
1926.1053(a)(22)(ii)They shall permit the employee using the device to ascend or descend without continually having to hold, push or pull any part of the device, leaving both hands free for climbing;
1926.1053(a)(22)(iii)They shall be activated within 2 feet (.61 m) after a fall occurs, and limit the descending velocity of an employee to 7 feet/sec. (2.1 m/sec.) or less;
1926.1053(a)(22)(iv)The connection between the carrier or lifeline and the point of attachment to the body belt or harness shall not exceed 9 inches (23 cm) in length.
1926.1053(a)(23)The mounting of ladder safety devices for fixed ladders shall conform to the following:
1926.1053(a)(23)(i)Mountings for rigid carriers shall be attached at each end of the carrier, with intermediate mountings, as necessary, spaced along the entire length of the carrier, to provide the strength necessary to stop employees' falls.
1926.1053(a)(23)(ii)Mountings for flexible carriers shall be attached at each end of the carrier. When the system is exposed to wind, cable guides for flexible carriers shall be installed at a minimum spacing of 25 feet (7.6 m) and maximum spacing of 40 feet (12.2 m) along the entire length of the carrier, to prevent wind damage to the system.
1926.1053(a)(23)(iii)The design and installation of mountings and cable guides shall not reduce the design strength of the ladder.
1926.1053(a)(24)The side rails of through or side-step fixed ladders shall extend 42 inches (1.1 m) above the top of the access level or landing platform served by the ladder. For a parapet ladder, the access level shall be the roof if the parapet is cut to permit passage through the parapet; if the parapet is continuous, the access level shall be the top of the parapet.
1926.1053(a)(25)For through-fixed-ladder extensions, the steps or rungs shall be omitted from the extension and the extension of the side rails shall be flared to provide not less than 24 inches (61 cm) nor more than 30 inches (76 cm) clearance between side rails. Where ladder safety devices are provided, the maximum clearance between side rails of the extensions shall not exceed 36 inches (91 cm).
1926.1053(a)(26)For side-step fixed ladders, the side rails and the steps or rungs shall be continuous in the extension.
1926.1053(a)(27)Individual-rung/step ladders, except those used where their access openings are covered with manhole covers or hatches, shall extend at least 42 inches (1.1 m) above an access level or landing platform either by the continuation of the rung spacings as horizontal grab bars or by providing vertical grab bars that shall have the same lateral spacing as the vertical legs of the rungs.
1926.1053(b)Use. The following requirements apply to the use of all ladders, including job-made ladders, except as otherwise indicated:
1926.1053(b)(1)When portable ladders are used for access to an upper landing surface, the ladder side rails shall extend at least 3 feet (.9 m) above the upper landing surface to which the ladder is used to gain access; or, when such an extension is not possible because of the ladder's length, then the ladder shall be secured at its top to a rigid support that will not deflect, and a grasping device, such as a grabrail, shall be provided to assist employees in mounting and dismounting the ladder. In no case shall the extension be such that ladder deflection under a load would, by itself, cause the ladder to slip off its support.
1926.1053(b)(2)Ladders shall be maintained free of oil, grease, and other slipping hazards.
1926.1053(b)(3)Ladders shall not be loaded beyond the maximum intended load for which they were built, nor beyond their manufacturer's rated capacity.
1926.1053(b)(4)Ladders shall be used only for the purpose for which they were designed.
1926.1053(b)(5)(i)Non-self-supporting ladders shall be used at an angle such that the horizontal distance from the top support to the foot of the ladder is approximately one-quarter of the working length of the ladder (the distance along the ladder between the foot and the top support).
1926.1053(b)(5)(ii)Wood job-made ladders with spliced side rails shall be used at an angle such that the horizontal distance is one-eighth the working length of the ladder.
1926.1053(b)(5)(iii)Fixed ladders shall be used at a pitch no greater than 90 degrees from the horizontal, as measured to the back side of the ladder.
1926.1053(b)(6)Ladders shall be used only on stable and level surfaces unless secured to prevent accidental displacement.
1926.1053(b)(7)Ladders shall not be used on slippery surfaces unless secured or provided with slip-resistant feet to prevent accidental displacement. Slip-resistant feet shall not be used as a substitute for care in placing, lashing, or holding a ladder that is used upon slippery surfaces including, but not limited to, flat metal or concrete surfaces that are constructed so they cannot be prevented from becoming slippery.
1926.1053(b)(8)Ladders placed in any location where they can be displaced by workplace activities or traffic, such as in passageways, doorways, or driveways, shall be secured to prevent accidental displacement, or a barricade shall be used to keep the activities or traffic away from the ladder.
1926.1053(b)(9)The area around the top and bottom of ladders shall be kept clear.
1926.1053(b)(10)The top of a non-self-supporting ladder shall be placed with the two rails supported equally unless it is equipped with a single support attachment.
1926.1053(b)(11)Ladders shall not be moved, shifted, or extended while occupied.
1926.1053(b)(12)Ladders shall have nonconductive siderails if they are used where the employee or the ladder could contact exposed energized electrical equipment, except as provided in §1926.955(b) and (c) of this part.
1926.1053(b)(13)The top or top step of a stepladder shall not be used as a step.
1926.1053(b)(14)Cross-bracing on the rear section of stepladders shall not be used for climbing unless the ladders are designed and provided with steps for climbing on both front and rear sections.
1926.1053(b)(15)Ladders shall be inspected by a competent person for visible defects on a periodic basis and after any occurrence that could affect their safe use.
1926.1053(b)(16)Portable ladders with structural defects, such as, but not limited to, broken or missing rungs, cleats, or steps, broken or split rails, corroded components, or other faulty or defective components, shall either be immediately marked in a manner that readily identifies them as defective, or be tagged with "Do Not Use" or similar language, and shall be withdrawn from service until repaired.
1926.1053(b)(17)Fixed ladders with structural defects, such as, but not limited to, broken or missing rungs, cleats, or steps, broken or split rails, or corroded components, shall be withdrawn from service until repaired. The requirement to withdraw a defective ladder from service is satisfied if the ladder is either:
1926.1053(b)(17)(i)Immediately tagged with "Do Not Use" or similar language,
1926.1053(b)(17)(ii)Marked in a manner that readily identifies it as defective;
1926.1053(b)(17)(iii)Or blocked (such as with a plywood attachment that spans several rungs).
1926.1053(b)(18)Ladder repairs shall restore the ladder to a condition meeting its original design criteria, before the ladder is returned to use.
1926.1053(b)(19)Single-rail ladders shall not be used.
1926.1053(b)(20)When ascending or descending a ladder, the user shall face the ladder.
1926.1053(b)(21)Each employee shall use at least one hand to grasp the ladder when progressing up and/or down the ladder.
1926.1053(b)(22)An employee shall not carry any object or load that could cause the employee to lose balance and fall.

## Slide 11: No incline una escalera de tijera
La escalera de tijera no está diseñada para estar inclinada.
El ángulo de los peldaños no está nivelado cuando se coloca a 4:1.
La pata de apoyo puede entrar en contacto con el suelo y hacer que el peldaño se levante.
Andamios, escaleras móviles y jirafas
Notes: Picture 1 & 2 depicts improper use of a step ladderOSHA Interpretation Letter #200801220-8196
Re: Using a stepladder as a non-self-supporting ladder
Would the use of a stepladder as described above violate 29 CFR 1926.1053(b)(4)? If so, would such use be a de minimis violation?
Answer: In 29 CFR 1926 Subpart X, 1926.1053(b)(4) states:
Ladders shall be used only for the purpose for which they were designed. [Emphasis added]
Thus, using a stepladder as a non-self-supporting ladder would violate §1926.1053(b)(4) if the ladder were not designed for that purpose.
The particular design of a stepladder varies from manufacturer to manufacturer. Therefore, whether or not the scenario you describe
constitutes a violation of §1926.1053(b)(4) would depend on whether such use is consistent with the purpose intended by the manufacturer

## Slide 12: ¡No se pare en el peldaño superior ni junto a él!
¡Respete las etiquetas!
¡NO!
Andamios, escaleras móviles y jirafas
Notes: Picture 1 depicts a label off of a ladder
Picture 2 depicts a worker on the top plate of a step ladder

## Slide 13: Trabajar desde una escalera móvil recta
Colóquese siempre de frente a la escalera.
Mantenga una mano en la escalera para sujetarse.
No trabaje en los cuatro peldaños superiores.
Trabaje al mismo nivel.
Andamios, escaleras móviles y jirafas

## Slide 14: Establezca el ángulo correcto
La distancia de la parte inferior de la escalera móvil a la pared debe ser de un cuarto de la altura de trabajo de la escalera.
Un brazo extendido es una medida cercana.
Andamios, escaleras móviles y jirafas

## Slide 15: Acceso correcto a escaleras móviles
Las escaleras móviles deben estar aseguradas.
Las vías de acceso deben estar protegidas.
Las escaleras móviles deben extenderse 3 pies por encima de la superficie de apoyo o se debe proporcionar una barra de agarre adecuada.
Andamios, escaleras móviles y jirafas
Notes: Set up ladders on level, stable ground and not in fronast of closed doors
1926.1053(b)(13)The top or top step of a stepladder shall not be used as a step.

## Slide 16: Vías de acceso por escalera móvil
Se recomiendan barandas desplazadas.
Atención a los peligros de tropiezo en la parte superior de las escaleras móviles y los peldaños.
Andamios, escaleras móviles y jirafas
Notes: Ladderways and stairwells should planned well in advance to ensure their safe operation from phase to phase.
Additionally, proper guardrails and handrail systems should be installed and maintained throughout the project.
Offset guardrail systems are an ideal way to protect areas where access must be made through perimeter protection.

## Slide 17: Ascenso a una escalera vertical
Las escaleras verticales altas deben estar equipadas con dispositivos para subir.
Las jaulas de escaleras son necesarias después de que una escalera alcance los 24 pies si no se utilizan dispositivos para subir escaleras.
Andamios, escaleras móviles y jirafas
Notes: 1926.1053(a)(19) Where the total length of a climb equals or exceeds 24 feet (7.3 m), fixed ladders shall be equipped with one of the following:1926.1053(a)(19)(i) Ladder safety devices; or1926.1053(a)(19)(ii) Self-retracting lifelines, and rest platforms at intervals not to exceed 150 feet (45.7 m); or1926.1053(a)(19)(iii) A cage or well, and multiple ladder sections, each ladder section not to exceed 50 feet (15.2 m) in length. Ladder sections shall be offset from adjacent sections, and landing platforms shall be provided at maximum intervals of 50 feet (15.2 m).

## Slide 18: Protección contra caídas en jirafas 1
Los requisitos de la OSHA son OBLIGATORIOS.
La plataforma de trabajo móvil (MEWP) es una práctica recomendada.
Andamios, escaleras móviles y jirafas
Notes: “Under subpart L, employers must ensure that employees tie off at all times when working from an aerial lift [§1926.453(b)(2)(v)].”
August 22, 2011 MEMORANDUM FOR: REGIONAL ADMINISTRATORS, FROM: JAMES G. MADDUX, Director Directorate of Construction
SUBJECT: Fall protection on aerial lifts during construction activities.
Tie-off is required even at low heights to restraint from possible ejection even especially when traveling

## Slide 19: Protección contra caídas en jirafas 2
Se requieren arneses y cuerdas de anclaje.
Jirafa con cesta
No se requieren cuerdas de anclaje, a menos que el trabajador se levante desde el suelo.
Jirafas de tijera
Cierre siempre las cadenas o puertas de la plataforma de la jirafa. No se suba, no se pare ni se incline sobre las barandas.
Andamios, escaleras móviles y jirafas
Notes: “Under subpart L, employers must ensure that employees tie off at all times when working from an aerial lift [§1926.453(b)(2)(v)].”
August 22, 2011 MEMORANDUM FOR: REGIONAL ADMINISTRATORS, FROM: JAMES G. MADDUX, Director Directorate of Construction
SUBJECT: Fall protection on aerial lifts during construction activities.
Tie-off is required even at low heights to restraint from possible ejection even especially when traveling

## Slide 20: No pararse en las barandas
No se suba a las barandas ni trabaje desde ellas.
Andamios, escaleras móviles y jirafas

## Slide 21: Jirafas con cestas
Los trabajadores de las jirafas con cestas deben llevar arnés y estar atados a los anclajes adecuados.
La cuerda de anclaje debe colocarse de tal forma que el trabajador no pueda salir despedido de la cesta.
Los trabajadores nunca deben subirse a las barandas de una jirafa.
Andamios, escaleras móviles y jirafas
Notes: OSHA Interp. 8/22/11 Under subpart L, employers must ensure that employees tie off at all times when working from an aerial lift [§1926.453(b)(2)(v)]. Employers must ensure that employees using personal fall arrest systems while working on aerial lifts at heights six feet or more above a lower level comply with §1926.502(d) of subpart M, specifically:
Personal fall arrest systems, when stopping a fall, shall: ... (iii) be rigged such that an employee can neither free fall more than 6 feet (1.8 m), nor contact any lower level. [§1926.502(d)(16)(iii)] However, §1926.502(d) does not require employers to comply with manufacturer's instructions when using personal fall arrest systems. To cite §1926.502(d)(16)(iii), the facts must show that the personal fall arrest system would permit a free fall of more than six feet or would permit contact with a lower level - and not base this conclusion solely on information provided by the manufacturer. As has been the Agency's longstanding policy, an employer may comply with OSHA's fall protection requirements for aerial lifts in one of three ways:
Use of a body belt with a tether anchored to the boom or basket (fall restraint system),
Use of a body harness with a tether (fall restraint system), or
Use of a body harness with a lanyard (fall arrest system).

## Slide 22: ¿Tiene preguntas?
Andamios, escaleras móviles y jirafas