## Slide 1: Introduction
  Fatality rate twice as high as other construction workers and eight times higher than the average worker
  Source: CFOI – Census of Fatal Occupational Injuries
Notes: <number>
Focus Four + one – 80-90% of your fatalities and loss dollars. The focus is not on equipment damage, vehicle damage, it is directly on the Highway Worker who is 2-4 times more likely to be killed working on a road than on a normal construction project due to the serious nature of the work that they are performing on major and minor roads in the U.S.
Planning is always the basis for success.
Pre-planning begins when the bid is assembled. At that point, major risk control issues should be identified. They should include the need for MOT and any special skills the workers might need that require specialized training, such as “Work Zone Awareness” or “Confined Space Entrant.” Identify what pieces of equipment will be required and how many operators are needed for each. Do your workers have the proper certifications and authorizations for the equipment?
Like doing a material take-off, the estimate should be reviewed and identified safety issues placed on paper.
Every worker's education should include the idea that they ask themselves, "How can I do this without injury or accident?" before starting any task. Learning to trust their own answers will help them prevent accidents and injuries to themselves.

## Slide 2: Introduction
Annually on highway-related projects:
  More than 100 fatalities
  20,000 injuries
  Fatality rate twice as high as other construction workers
  Workers and motorists at risk
Notes: <number>
Focus Four + one – 80-90% of your fatalities and loss dollars. The focus is not on equipment damage, vehicle damage, it is directly on the Highway Worker who is 2-4 times more likely to be killed working on a road than on a normal construction project due to the serious nature of the work that they are performing on major and minor roads in the U.S.
Planning is always the basis for success.
Pre-planning begins when the bid is assembled. At that point, major risk control issues should be identified. They should include the need for MOT and any special skills the workers might need that require specialized training, such as “Work Zone Awareness” or “Confined Space Entrant.” Identify what pieces of equipment will be required and how many operators are needed for each. Do your workers have the proper certifications and authorizations for the equipment?
Like doing a material take-off, the estimate should be reviewed and identified safety issues placed on paper.
Every worker's education should include the idea that they ask themselves, "How can I do this without injury or accident?" before starting any task. Learning to trust their own answers will help them prevent accidents and injuries to themselves.

## Slide 3: Introduction
Webinar Learning Objectives
Understand the key exposures that kill and maim 90% of all highway workers
Understand the best controls to eliminate and minimize these exposures
Understand the "Focus Four + One" concept and hierarchy of safety controls
Be able to navigate and effectively use the multiple parts of this safety program to train subcontractors, management, and employees
Feel empowered to effectively train supervisors or employees performing grading, utility, bridge, asphalt, concrete, traffic control and demolition operations to plan safe operations safe while working on or adjacent to highways in the United States.
Notes: <number>
Focus Four + one – 80-90% of your fatalities and loss dollars. The focus is not on equipment damage, vehicle damage, it is directly on the Highway Worker who is 2-4 times more likely to be killed working on a road than on a normal construction project due to the serious nature of the work that they are performing on major and minor roads in the U.S.
Planning is always the basis for success.
Pre-planning begins when the bid is assembled. At that point, major risk control issues should be identified. They should include the need for MOT and any special skills the workers might need that require specialized training, such as “Work Zone Awareness” or “Confined Space Entrant.” Identify what pieces of equipment will be required and how many operators are needed for each. Do your workers have the proper certifications and authorizations for the equipment?
Like doing a material take-off, the estimate should be reviewed and identified safety issues placed on paper.
Every worker's education should include the idea that they ask themselves, "How can I do this without injury or accident?" before starting any task. Learning to trust their own answers will help them prevent accidents and injuries to themselves.

## Slide 4: Highway Worker Safety Program
History
AGC Safety Committee & Zurich
AGC Highway Division – Comprehensive Highway Safety Product
Participation
Over 100 highway contractor safety professionals and companies
Notes: <number>
Discuss history of the relationship of Zurich and the AGC as it relates to STIPP, STIPP Success -18% reduction in losses and participation/sponsorship of the AGC safety committee
Pride in loving what I do, in being a part of creating something that can really have an impact to save lives, reduce losses, and make companies better.
During the filming over the last year a number of companies step forward with time and resources to allow us to film and create the footage we needed to make this product. Thank you to these companies and their loss control personnel who helped get the footage we needed.
Norman Walton and the AGC Highway Division about producing a new safety product – Comprehensive, Can be used by all size and scope of Highway contractor. Targeted towards reducing worker losses.
During over two years of the development of the Highway Worker Safety Program there have been many people who have worked at these committee meetings, remotely, between the conference calls, and we have been rewarded with a great safety product that I believe meets the criteria established by the highway division.
Every person on this committee who participated can really be proud of this product and thank you for all of your hard work!

## Slide 5: Highway Worker Safety Program
The Highway Worker Safety Program is a comprehensive training program that focuses on the leading causes of fatality and injury for highway workers.
The HWSP program is set up so that it can be used by both the large general contractor and the small sub or specialty contractor working on your project. Great training program for all types of contractors including subs working on your highway project.
Notes: <number>
Comprehensive training program that concentrates on the leading causes of fatality and serious injury for highway workers – period
Set up so a small contractor who may have a relatively small budget for safety and take parts of this program and show it on the back of a pickup or in a class room and be able to discuss the critical exposures that affect their workers.
Or for the Large GC or construction manager who may have any number of subcontractors doing everything from striping to guard rail installation to bridge building who wants to offer or assist these subs and their own managers in planning and recognizing the loss leaders for their projects.

## Slide 6
What does the Highway Worker Safety Program include?
DVD with interactive Video Components
DVD ROM with
Editable PowerPoint Program - 298 slides
Instructor Guide – 120 pages
Participant’s Manual - 80+ pages
Resource page with links to other web pages
Notes: There is so much information in this program and it is so easy to access that it can almost overwhelm a safety professional trying to see where to start.
I am convinced that this is the way of the present & future as far as offering resources and interactive training.
DVD – Interactive - quizzes
DVD Rom – Customizable PowerPoint.
Instructor guide – 120 pages including information on training adult learners.
Participant guide with quizzes

## Slide 7: Key issues that affect all
Planning & Communication
Traffic Control
Visibility
Night Work
Environmental Hazards
Notes: Five key issues the safety committee members felt affected all highway contractors.

## Slide 8: Navigation of the DVD
The navigation of the DVD is totally interactive and the next few slides show the navigation.
Notes: Five key issues the safety committee members felt affected all highway contractors.

## Slide 9: Highway Worker Safety Program
Notes: The complete program that will be available through Zurich includes a DVD, a DVD ROM, one written instructor manual, and five trainee guides. When you first present it to your customer you might want to mention that additional trainee guides can be printed or ordered through the AGC of America. At present Zurich is ordering the packages and not the separate components of the program.
This safety program that you are providing to your customer includes approximately 90 minutes of video, a PowerPoint presentation with 297 slides with imbedded video links, and an editable PowerPoint on the DVD ROM that allows your customer to customize this, including their own work pictures and key exposures
Written materials include a 130 page instructor’s guide and 96 page participant’s manual. The instructor’s guide corresponds with the PowerPoint since the PowerPoint is used to assist the instructor with teaching various portions of the program. The participant’s manual follows along with the video scripts and assists the instructor in providing the learning objects of the program.
One of the great things about the design of this program is that it is interactive. What does this mean? It means that it is very user friendly and allows you to play portions of the program or the entire program. It also means that elements of video are imbedded in the PowerPoint which allows your customer to take their workers right into the field and show them the safety element being taught on the PowerPoint.
Additionally the resource page has real web links that when accessed while working online allow the customer to access that resource directly from the product.

## Slide 10: Highway Worker Safety Program
Notes: The complete program that will be available through Zurich includes a DVD, a DVD ROM, one written instructor manual, and five trainee guides. When you first present it to your customer you might want to mention that additional trainee guides can be printed or ordered through the AGC of America. At present Zurich is ordering the packages and not the separate components of the program.
This safety program that you are providing to your customer includes approximately 90 minutes of video, a PowerPoint presentation with 297 slides with imbedded video links, and an editable PowerPoint on the DVD ROM that allows your customer to customize this, including their own work pictures and key exposures
Written materials include a 130 page instructor’s guide and 96 page participant’s manual. The instructor’s guide corresponds with the PowerPoint since the PowerPoint is used to assist the instructor with teaching various portions of the program. The participant’s manual follows along with the video scripts and assists the instructor in providing the learning objects of the program.
One of the great things about the design of this program is that it is interactive. What does this mean? It means that it is very user friendly and allows you to play portions of the program or the entire program. It also means that elements of video are imbedded in the PowerPoint which allows your customer to take their workers right into the field and show them the safety element being taught on the PowerPoint.
Additionally the resource page has real web links that when accessed while working online allow the customer to access that resource directly from the product.

## Slide 11: Highway Worker Safety Program
Notes: The complete program that will be available through Zurich includes a DVD, a DVD ROM, one written instructor manual, and five trainee guides. When you first present it to your customer you might want to mention that additional trainee guides can be printed or ordered through the AGC of America. At present Zurich is ordering the packages and not the separate components of the program.
This safety program that you are providing to your customer includes approximately 90 minutes of video, a PowerPoint presentation with 297 slides with imbedded video links, and an editable PowerPoint on the DVD ROM that allows your customer to customize this, including their own work pictures and key exposures
Written materials include a 130 page instructor’s guide and 96 page participant’s manual. The instructor’s guide corresponds with the PowerPoint since the PowerPoint is used to assist the instructor with teaching various portions of the program. The participant’s manual follows along with the video scripts and assists the instructor in providing the learning objects of the program.
One of the great things about the design of this program is that it is interactive. What does this mean? It means that it is very user friendly and allows you to play portions of the program or the entire program. It also means that elements of video are imbedded in the PowerPoint which allows your customer to take their workers right into the field and show them the safety element being taught on the PowerPoint.
Additionally the resource page has real web links that when accessed while working online allow the customer to access that resource directly from the product.

## Slide 12: Highway Worker Safety Program
Notes: The complete program that will be available through Zurich includes a DVD, a DVD ROM, one written instructor manual, and five trainee guides. When you first present it to your customer you might want to mention that additional trainee guides can be printed or ordered through the AGC of America. At present Zurich is ordering the packages and not the separate components of the program.
This safety program that you are providing to your customer includes approximately 90 minutes of video, a PowerPoint presentation with 297 slides with imbedded video links, and an editable PowerPoint on the DVD ROM that allows your customer to customize this, including their own work pictures and key exposures
Written materials include a 130 page instructor’s guide and 96 page participant’s manual. The instructor’s guide corresponds with the PowerPoint since the PowerPoint is used to assist the instructor with teaching various portions of the program. The participant’s manual follows along with the video scripts and assists the instructor in providing the learning objects of the program.
One of the great things about the design of this program is that it is interactive. What does this mean? It means that it is very user friendly and allows you to play portions of the program or the entire program. It also means that elements of video are imbedded in the PowerPoint which allows your customer to take their workers right into the field and show them the safety element being taught on the PowerPoint.
Additionally the resource page has real web links that when accessed while working online allow the customer to access that resource directly from the product.

## Slide 13: Highway Worker Safety Program
Notes: The complete program that will be available through Zurich includes a DVD, a DVD ROM, one written instructor manual, and five trainee guides. When you first present it to your customer you might want to mention that additional trainee guides can be printed or ordered through the AGC of America. At present Zurich is ordering the packages and not the separate components of the program.
This safety program that you are providing to your customer includes approximately 90 minutes of video, a PowerPoint presentation with 297 slides with imbedded video links, and an editable PowerPoint on the DVD ROM that allows your customer to customize this, including their own work pictures and key exposures
Written materials include a 130 page instructor’s guide and 96 page participant’s manual. The instructor’s guide corresponds with the PowerPoint since the PowerPoint is used to assist the instructor with teaching various portions of the program. The participant’s manual follows along with the video scripts and assists the instructor in providing the learning objects of the program.
One of the great things about the design of this program is that it is interactive. What does this mean? It means that it is very user friendly and allows you to play portions of the program or the entire program. It also means that elements of video are imbedded in the PowerPoint which allows your customer to take their workers right into the field and show them the safety element being taught on the PowerPoint.
Additionally the resource page has real web links that when accessed while working online allow the customer to access that resource directly from the product.

## Slide 14: Navigation
Next is the navigation shown as the menu’s on the DVD’s
Highway Worker Safety Program

## Slide 19
THIS WILL BE THE VIDEO SLIDE

## Slide 20: Introduction Focus Four Plus One
Highway Worker Safety Program
  “Focus Four Plus One”
    Struck-by hazards
    Fall hazards
    Caught-In-Between hazards
    Electrical hazards
    Soft tissue injuries
Common exposures
Notes: <number>
BLS Statistics.
Soft tissue injuries are the leading cause of lost time injuries for workers.

## Slide 21: Introduction Hierarchy of Controls
Best-practice controls – the Hierarchy of Control
Each section will discuss appropriate controls, ranked in order of effectiveness:
  Engineering controls – remove or eliminate
  Administrative controls – train or prohibit access
  Personal Protective Equipment – the least effective, and only after the above are employed
Notes: <number>

## Slide 22: Introduction Task-specific sections
Task-specific Hazards and Controls
  Traffic control
  Asphalt paving & patching operations
  Bridge construction work
  Concrete paving & patching operations
  Demolition operations
  Utility & drainage operations
  Grading & earthmoving operations
  Short-term & mobile operations

## Slide 23: Highway Worker Safety Program Components
Notes: The complete program that will be available through Zurich includes a DVD, a DVD ROM, one written instructor manual, and five trainee guides. When you first present it to your customer you might want to mention that additional trainee guides can be printed or ordered through the AGC of America. At present Zurich is ordering the packages and not the separate components of the program.
This safety program that you are providing to your customer includes approximately 90 minutes of video, a PowerPoint presentation with 297 slides with imbedded video links, and an editable PowerPoint on the DVD ROM that allows your customer to customize this, including their own work pictures and key exposures
Written materials include a 130 page instructor’s guide and 96 page participant’s manual. The instructor’s guide corresponds with the PowerPoint since the PowerPoint is used to assist the instructor with teaching various portions of the program. The participant’s manual follows along with the video scripts and assists the instructor in providing the learning objects of the program.
One of the great things about the design of this program is that it is interactive. What does this mean? It means that it is very user friendly and allows you to play portions of the program or the entire program. It also means that elements of video are imbedded in the PowerPoint which allows your customer to take their workers right into the field and show them the safety element being taught on the PowerPoint.
Additionally the resource page has real web links that when accessed while working online allow the customer to access that resource directly from the product.

## Slide 24: Highway Worker Safety Program Components
Notes: The complete program that will be available through Zurich includes a DVD, a DVD ROM, one written instructor manual, and five trainee guides. When you first present it to your customer you might want to mention that additional trainee guides can be printed or ordered through the AGC of America. At present Zurich is ordering the packages and not the separate components of the program.
This safety program that you are providing to your customer includes approximately 90 minutes of video, a PowerPoint presentation with 297 slides with imbedded video links, and an editable PowerPoint on the DVD ROM that allows your customer to customize this, including their own work pictures and key exposures
Written materials include a 130 page instructor’s guide and 96 page participant’s manual. The instructor’s guide corresponds with the PowerPoint since the PowerPoint is used to assist the instructor with teaching various portions of the program. The participant’s manual follows along with the video scripts and assists the instructor in providing the learning objects of the program.
One of the great things about the design of this program is that it is interactive. What does this mean? It means that it is very user friendly and allows you to play portions of the program or the entire program. It also means that elements of video are imbedded in the PowerPoint which allows your customer to take their workers right into the field and show them the safety element being taught on the PowerPoint.
Additionally the resource page has real web links that when accessed while working online allow the customer to access that resource directly from the product.

## Slide 25: Highway Worker Safety Program Components
Notes: The complete program that will be available through Zurich includes a DVD, a DVD ROM, one written instructor manual, and five trainee guides. When you first present it to your customer you might want to mention that additional trainee guides can be printed or ordered through the AGC of America. At present Zurich is ordering the packages and not the separate components of the program.
This safety program that you are providing to your customer includes approximately 90 minutes of video, a PowerPoint presentation with 297 slides with imbedded video links, and an editable PowerPoint on the DVD ROM that allows your customer to customize this, including their own work pictures and key exposures
Written materials include a 130 page instructor’s guide and 96 page participant’s manual. The instructor’s guide corresponds with the PowerPoint since the PowerPoint is used to assist the instructor with teaching various portions of the program. The participant’s manual follows along with the video scripts and assists the instructor in providing the learning objects of the program.
One of the great things about the design of this program is that it is interactive. What does this mean? It means that it is very user friendly and allows you to play portions of the program or the entire program. It also means that elements of video are imbedded in the PowerPoint which allows your customer to take their workers right into the field and show them the safety element being taught on the PowerPoint.
Additionally the resource page has real web links that when accessed while working online allow the customer to access that resource directly from the product.

## Slide 26: Highway Worker Safety Program Components
Notes: The complete program that will be available through Zurich includes a DVD, a DVD ROM, one written instructor manual, and five trainee guides. When you first present it to your customer you might want to mention that additional trainee guides can be printed or ordered through the AGC of America. At present Zurich is ordering the packages and not the separate components of the program.
This safety program that you are providing to your customer includes approximately 90 minutes of video, a PowerPoint presentation with 297 slides with imbedded video links, and an editable PowerPoint on the DVD ROM that allows your customer to customize this, including their own work pictures and key exposures
Written materials include a 130 page instructor’s guide and 96 page participant’s manual. The instructor’s guide corresponds with the PowerPoint since the PowerPoint is used to assist the instructor with teaching various portions of the program. The participant’s manual follows along with the video scripts and assists the instructor in providing the learning objects of the program.
One of the great things about the design of this program is that it is interactive. What does this mean? It means that it is very user friendly and allows you to play portions of the program or the entire program. It also means that elements of video are imbedded in the PowerPoint which allows your customer to take their workers right into the field and show them the safety element being taught on the PowerPoint.
Additionally the resource page has real web links that when accessed while working online allow the customer to access that resource directly from the product.

## Slide 27: Highway Worker Safety Program Components
Notes: The complete program that will be available through Zurich includes a DVD, a DVD ROM, one written instructor manual, and five trainee guides. When you first present it to your customer you might want to mention that additional trainee guides can be printed or ordered through the AGC of America. At present Zurich is ordering the packages and not the separate components of the program.
This safety program that you are providing to your customer includes approximately 90 minutes of video, a PowerPoint presentation with 297 slides with imbedded video links, and an editable PowerPoint on the DVD ROM that allows your customer to customize this, including their own work pictures and key exposures
Written materials include a 130 page instructor’s guide and 96 page participant’s manual. The instructor’s guide corresponds with the PowerPoint since the PowerPoint is used to assist the instructor with teaching various portions of the program. The participant’s manual follows along with the video scripts and assists the instructor in providing the learning objects of the program.
One of the great things about the design of this program is that it is interactive. What does this mean? It means that it is very user friendly and allows you to play portions of the program or the entire program. It also means that elements of video are imbedded in the PowerPoint which allows your customer to take their workers right into the field and show them the safety element being taught on the PowerPoint.
Additionally the resource page has real web links that when accessed while working online allow the customer to access that resource directly from the product.

## Slide 28: Highway Worker Safety Program Components
Notes: The complete program that will be available through Zurich includes a DVD, a DVD ROM, one written instructor manual, and five trainee guides. When you first present it to your customer you might want to mention that additional trainee guides can be printed or ordered through the AGC of America. At present Zurich is ordering the packages and not the separate components of the program.
This safety program that you are providing to your customer includes approximately 90 minutes of video, a PowerPoint presentation with 297 slides with imbedded video links, and an editable PowerPoint on the DVD ROM that allows your customer to customize this, including their own work pictures and key exposures
Written materials include a 130 page instructor’s guide and 96 page participant’s manual. The instructor’s guide corresponds with the PowerPoint since the PowerPoint is used to assist the instructor with teaching various portions of the program. The participant’s manual follows along with the video scripts and assists the instructor in providing the learning objects of the program.
One of the great things about the design of this program is that it is interactive. What does this mean? It means that it is very user friendly and allows you to play portions of the program or the entire program. It also means that elements of video are imbedded in the PowerPoint which allows your customer to take their workers right into the field and show them the safety element being taught on the PowerPoint.
Additionally the resource page has real web links that when accessed while working online allow the customer to access that resource directly from the product.

## Slide 29: Navigation
Next is the navigation shown as the menu’s on the DVD’s
Highway Worker Safety Program

## Slide 35
THIS WILL BE THE VIDEO SLIDE

## Slide 36: Introduction Other Training Issues
This program is not designed to address more specific or comprehensive training needs, such as (but not limited to):
  Scaffolding
  Fall protection
  Ladders
  Cranes & rigging
  Fire prevention
  Confined space
  Aerial work platforms
  Forklifts
  Hand & power tools
Notes: <number>

## Slide 37: Highway Worker Safety Program
This Highway Worker Safety program is intended to increase awareness of certain factors that may contribute to highway worker injuries and fatalities among construction craft workers and to suggest practices that may reduce the risk of such injuries. This program is not intended to provide specific guidance to any one construction company or for any one construction project. This program does not address the entire range of activities or conditions found in the construction industry, or suggest that other approaches to the risk of highway worker injury do not merit equal consideration. The information that this program conveys is necessarily general in nature.
While certain practices appear to be desirable, none can guarantee that highway worker injuries will not occur. This program does not create any obligations, or establish any specific standards or guidelines, for managing the risk of such injuries. It is not an exhaustive or complete treatment of its subject matter.
In making this program available, neither Zurich Services Corporation (hereinafter “Zurich”) nor the Associated General Contractors of America, Inc. (hereinafter “AGC”), undertakes to perform services for or on behalf of any party, whether for that party’s own protection or for the protection of others. Neither Zurich nor AGC accepts any delegation of duties, or makes any warranties, whether express or implied, or assumes any liability whatsoever for reliance on this program or its contents.
This Highway Worker Safety program does not specify any course of conduct or set of practices required by law or regulation, or convey legal, medical or other professional advice.
Notes: <number>
Discuss history of the relationship of Zurich and the AGC as it relates to STIPP, STIPP Success -18% reduction in losses and participation/sponsorship of the AGC safety committee
Pride in loving what I do, in being a part of creating something that can really have an impact to save lives, reduce losses, and make companies better.
During the filming over the last year a number of companies step forward with time and resources to allow us to film and create the footage we needed to make this product. Thank you to these companies and their loss control personnel who helped get the footage we needed.
Norman Walton and the AGC Highway Division about producing a new safety product – Comprehensive, Can be used by all size and scope of Highway contractor. Targeted towards reducing worker losses.
During over two years of the development of the Highway Worker Safety Program there have been many people who have worked at these committee meetings, remotely, between the conference calls, and we have been rewarded with a great safety product that I believe meets the criteria established by the highway division.
Every person on this committee who participated can really be proud of this product and thank you for all of your hard work!